## Slide 1: STAR Algorithm and Data Products (ADP) Beta Release Suomi NPP Surface Albedo EDR Product
Prepared by
Yunyue Yu, Dongdong Wang, Leslie Belsma
June 25th, 2013

## Slide 2: STAR ADP LSA EDR Team Members
Ivan Csiszar (NOAA/NESDIS/STAR) STAR Land EDRs Chair, management
Jeff Privette (NOAA/NESDIS/NCDC) product validation Lead
Yunyue Yu (NOAA/NESDIS/STAR) STAR LSA EDR lead, product monitoring and validation; algorithm development, project management
Shunlin Liang(UMD/Geography) UMD PI, algorithm development, product validation
Dongdong Wang(UMD/Geography) algorithm development, product validation
Crystal Schaaf (UMB) UMB PI, algorithm development, product validation
Zhuosen Wang (UMB) algorithm development, product validation
Leslie Belsma (JPSS/DPA, Aerospace Corp) Algorithm Manager (JAM) for Land
Youhua Tang (NOAA Affiliate, SciTech/IMSG) ADL verification
Michael EK (NOAA/EMC/NCEP) user readiness
Jesse Meng (NOAA Affiliate) user readiness

## Slide 3: Background of SA Product
Surface albedo is produced as Environmental Data Record (EDR) .
Surface albedo EDR (VIIRS-SA-EDR) has the global coverage, including land surface albedo (LSA), ocean surface albedo (OSA) and sea-ice surface albedo (ISA). Beta maturity is based on validation of LSA.
Two algorithms (Dark Pixel Sub-Algorithm (DPSA) and Bright Pixel Sub-Algorithm (BPSA)) implemented for LSA; DPSA uses the BRDF information from the 16-day gridded albedo IP to first calculate spectral albedo and then convert spectral albedo to broadband albedo using empirical models. BPSA directly estimate broadband albedo from VIIRS TOA radiance.
A LUT approach is applied for OSA, using solar zenith angle, aerosol optical thickness, wind speed and chlorophyll concentration as inputs.
The BPSA is currently used to generate LSA from VIIRS. Several improvements have been made since launch.
VIIRS-SA-EDR product is expected to be used by weather forecasting models, Agriculture monitoring, drought prediction and monitoring, ecosystem monitoring; climate studies etc approach is applied for ISA

## Slide 4: L1RD Requirements
Albedo EDR |  | 
Attribute | Threshold | Objective
Albedo Applicable Conditions: day time, Clear only |  | 
a. Horizontal Cell Size |  | 
Nadir | 4 km | 0.5 km
b. Mapping Uncertainty, 3 Sigma | 4km | 1 km
c. Measurement Range | 0 to 1.0 | 0 to 1.0
d. Measurement Precision ( 1 sigma) | 0.05 (albedo unit) | 0.02
e. Measurement Accuracy (bias) | 0.08 (albedo unit) | 0.0125
f. Refresh | At least 90% coverage of the globe every 24 hours (monthly average) . | 4 hrs.
Notes: Note: ( ) values are the most recent update request.

## Slide 5: Major Users of LSA product (Point of Contact)
U. S. Users*:
  NOAA National Weather Service Environmental Modeling Center (Michael EK, Jesse Meng, Weizhong Zheng )
  USDA Agricultural Research Services(Martha Anderson)
  USDA Forest Service (Brad Quayle)
  NOAA/NESDIS Center for Satellite Applications and Research (Jerry Zhan)
  NOAA/NESDIS National Climate Data Center (Peter Thorne)
  Academy -- University of Maryland (Konstantin Vinnikov, Shunlin Liang, Cezar Kongoli )
  Army Research Lab ( Kurt Preston)
Foreign Users
  EUMETSAT (Yves Govaerts)
  Météo France (Jean-Louis Roujean)
  Academy: Italy IASMA Research and Innovation Centre (Barbara Marcolla), Beijing Normal University (Qiang Liu)
  *The US USERs are to be verified.
Notes: The US USERs are to be verified.

## Slide 6: Overview of Albedo Products
6
RGB Image shows dense smoke (high absorption) in northwest, north central and central coastal portions of image.
VIIRS-SA-EDR is a full resolution product for each granule, under clear-sky condition.
VIIRS-SA-EDR is a combined from LSA, OSA, ISA
LSA is currently generated from the BPSA algorithm.
LSA has met the beta version product requirements:
  Early release product
  Initial calibration applied
  Minimally validated and may still contain significant errors (additional changes are expected)
  Available to allow users to gain familiarity with data formats and parameters
  Product is not appropriate as the basis for quantitative scientific publications, studies and applications
A couple of algorithm refinements have been made since launch.
  The BPSA regression LUT was updated.
  A new BRDF version of LUT is ready and will be implemented.
Assumptions of albedo validation:
  VIIRS SDR is calibrated and cloud/snow mask is reliable.
  OSA, ISA are equivalent or higher quality than LSA because they are more stable over space and time

## Slide 7: History of Algorithm changes/updates
Date Submitted | Update/DR# | Description | Status
4/30/12 | DR 4709 | Update pre-launch 2002 seeded data for BRDF Archival tiles because even after gridding is turned on, it will take many months for these tiles to be populated with VIIRS data. | Closed. CCR 474-CCR-12-0610 went into ops 10/12/12
4/30/12 | DR 4704 | The pre-launch LUT of BPSA regression coefficients used old spectral response functions. We generated a set of new regression coefficients after launch. This algorithm update is about replacing the old LUT with this new one and slightly adjusting some codes as needed | Closed. The results from the updated LUT was verified. CCR-12-0606,0889 into ops with Mx6.7
9/12/12 | DR 4901 | SA Jump in precision after Mx6.2. Cal/Val analysis of the Albedo EDR shows a substantial degradation of performance for data gathered after August 9th when Mx6.2 went operational. This might be caused by an incorrect LUT used for this algorithm. | Closed Did not occur after SA BPSA LUT DR4704 became operational in Mx6.7.
8/22/12 | DR 4882 | SA Fix BRDF Kernel Selection. BRDF derivation using a "best" fitting kernel model is selected from a multiple kernel combination approach. This is not necessary, and even may cause problems. Investigation shows that a fixed RossThick Li-Sparse Reciproral (RTLSR) kernel (which is the MODIS heritage) is the best approach for the VIIRS Gridded Albedo/BRDF derivation. | Closed.474-CCR-12-0607 passed AERB 16 Jan 13 Approved 16 Jan AERB for Mx7.1
3/28/13 | DR 7114 | 17-Day LSA GIP experienced failures in Mx6.7 due to the code was blindly using fill values for the coeff in the ProGipViirsGridToGridLSA when calculating Nbar, BlackSky, and WhiteSky causing the ProCmnScaler not to recognize the new fillvaules and causing a scale out of bound message | Closed.CCR_474-CCR-13-1031 passed AERB on17 May schedule for Mx8.0

## Slide 8: History of Algorithm changes/updates
Date Submitted | Update/DR# | Description | Status
7/7/11 | DR 4303 | IngMsdCoefficients_ViirsSurfAlbedoStruct has two problems. Not only does it need to be wrapped in a "pragma pack(4)", but it also contains several 'long' variables (which are 4 bytes on nppdev1, but 8 bytes on moddev64)... | Open - Not a science team issue
5/4/11 | DR 4265 | Surface Albedo Summary Quality flag does not count “fill” pixels. The summary quality flag is defined as "Exclusion Summary" and "Percent of pixels with one or more exclusion criteria flags" which does not meet the intent of the summary quality flag | Deferred
1/13/11 | DR 4187 | Surface Albedo Mission Quality Flag for Ice Concentration exclusion. The code outputs "fill" data for any ice fields that are less than 0.99 ice concentration, but no no quality flag to indicate why the data is "fill" from the ice concentration test. There is a spare bit available in the current output set that could be used to flag the test. | Deferred
1/13/11 | DR 4186 | Surface Albedo Quality indicator needs another level. Recommend a four level quality field:.. Good, Poor (degraded), Poor (excluded), and not calculated (excluded) - to replace the current three level field of Good, Poor, and not calculated. | Deferred
1/6/11 | DR 4183 | Surface Albedo Quality Flags are incorrect in the EDRPR. The code and EDRPR quality flag requirements differ. The problem comes about by the merging of the land, ice, and ocean albedo IP's that all tend to have different exclusions. | Closed 5/5/11 EDR PR updated.

## Slide 9: Processing for Global VIIRS-SA-EDR
Ocean Surface
Albedo IP
Land Surface
Albedo IP
Land/Water Mask
Albedo EDR Processing
Global VIIRS-SA-EDR Product
Sea-Ice Surface
Albedo IP

## Slide 10: Refinement to the BPSA algorithm
The BPSA LUT of regression coefficients was updated (DR4704).
Another version of LUT is generated and ready for implementation.
  Features:
    Using latest spectral response function
    Considering surface BRDF
  Improvements:
    Better accuracy when comparing with in situ data
    The problem of angular dependency is addressed

## Slide 11: Perform VIIRS Land Surface Albedo (LSA) Internal Evaluation
VIIRS LSA data evaluation
VIIRS LSA quality flag and metadata check
Upstream (SDRs, EDRs and IPs inputs) data check
Evaluation is performed at levels of
  Single granule map
  Granule aggregation map (temporal composite)
  Regional LSA map
  Global LSA composite map
Notes: Internal evaluation: check the data

## Slide 12: Example of Suomi NPP VIIRS LSA
VIIRS-SA-EDR data obtained on April 3 2012

## Slide 13: Example of Suomi NPP VIIRS LSA
Temporal aggregated map of surface albedo over continental USA

## Slide 14: Internal Evaluation summary
VIIRS-SA-EDR LSA data are checked and visually examined. Both the datasets of LSA and its quality flag are checked. The metadata associated with the data is also checked.
The data files are correctly generated. The internal evaluation reveals no issues with the data structure and file format.
There are 3 bytes pixel-level quality flag in total. Some fields of QF cannot correctly mark the retrieval quality. For example, some of filling values are marked as “good”.
Its upstream SDRs, EDRs and IPs (i.e., TOA reflectance, cloud mask) are also checked. It reveals no issues with upstream SDRs, EDRs and IPs.

## Slide 15: Perform VIIRS LSA Validation
External evaluation :
Evaluate temporal variability
  Over stable surfaces (e.g., desert)
  Comparing with variability from other methods (e.g. BRDF fitting)
Inter-comparison with MODIS albedo products
Validation against ground truth data
  Direct validation of daily albedo
  Comparison of 16-day mean albedo

## Slide 16: Evaluation of temporal variability of LSA
Residue of BRDF fitting, calculated as the difference between MODIS surface reflectance and BRF predicted from MODIS BRDF. The narrow-to-broadband conversion coefficients are used to covert spectral residues to the broadband residue
LSA retrieved from two LUT (Lambertian and BRDF LUT) at two desert sites. The spurious retrievals caused by undetected cloud and cloud shadow are excluded with the threshold of mean ± 0.05
The LSA retrievals over two Libya desert sites (Site 1: 24.42˚N 13.35˚E and Site 2: 26.45˚N, 14.08˚E) are used to illustrate the issue of temporal variability of LSA.

## Slide 17: Comparing VIIRS LSA with in situ and MODIS
Examples of comparison between LSA retrieved from VIIRS and MODIS and LSA measured at two SURFRAD sites

## Slide 18: Summary of validation
Site | VIIRS (BRDF LUT) |  |  | VIIRS (Lambertian LUT) |  |  | MODIS |  | 
 | R2 | RMSE | Bias | R2 | RMSE | Bias | R2 | RMSE | Bias
Bondville | 0.50 | 0.070 | -0.048 | 0.15 | 0.081 | -0.038 | 0.57 | 0.071 | -0.052
Fort Peck | 0.89 | 0.070 | 0.001 | 0.87 | 0.073 | -0.005 | 0.98 | 0.043 | -0.020
Goodwin Creek | 0.01 | 0.040 | -0.033 | 0.15 | 0.051 | -0.031 | 0.11 | 0.051 | -0.048
Desert Rock | 0.10 | 0.032 | 0.026 | 0.02 | 0.045 | 0.020 | 0.02 | 0.025 | -0.023
Penn State | 0.60 | 0.040 | -0.020 | 0.27 | 0.054 | -0.011 | 0.02 | 0.079 | -0.054
Sioux Falls | 0.89 | 0.064 | 0.004 | 0.82 | 0.066 | 0.007 | 0.87 | 0.059 | -0.001
Boulder | 0.96 | 0.029 | 0.011 | 0.91 | 0.034 | 0.012 | 0.79 | 0.047 | 0.002
Overall | 0.80 | 0.049 | -0.004 | 0.71 | 0.057 | -0.003 | 0.78 | 0.052 | -0.026
Summary of validation results at seven SURFRAD sites. Three satellite albedo data (VIIRS LSA from the Lambertian LUT, VIIRS LSA from the BRDF LUT and MODIS albedo) are validated against field measurements.

## Slide 19: Validation of 16-day mean LSA
Validation results of 16-day mean albedo from VIIRS BRDF LUT (top left), VIIRS Lambertian LUT (top right) and MODIS (bottom), using data from 2012 non-snow seasons (May-September) at seven SURFRAD sites.

## Slide 20: Maps of 16-day mean albedo
Contiguous US maps of 16-day mean LSA from VIIRS BRDF LUT (top) and MODIS (bottom), during DOY 145-160, 2012

## Slide 21: Comparison between VIIRS and MODIS albedo
Comparing 16-day mean VIIRS albedo from BRDF LUT (top) and Lambertian LUT (bottom) with MODIS blue-sky albedo. Data are limited to those with at least 8 clear-day observations during the composite period of 16 days.

## Slide 22: Evaluation/Validation Conclusion
The individual LSA retrieval from the current BPSA algorithm shows the problem of angular dependency.
A new BRDF LUT is developed. The variations of albedo retrievals from the BRDF LUT are reduced significantly. The variation is comparable with the reflectance residue of BRDF fitting.
VIIRS LSA retrievals agree well with the MODIS albedo products. Comparison with field measurements at seven SURFRAD sites shows that VIIRS LSA retrieved from the BRDF LUT has a R2 value of 0.80 and root mean squared error of 0.049, better than MODIS albedo products.
The BRDF LUT generates a small negative bias of -0.004, whereas the MODIS albedo is underestimated with a larger bias of -0.026.
Notes: Check with Yuling for the numbers

## Slide 23: Known Issues
The current BPSA LUT implemented in CLASS doesn’t consider surface BRDF. This leads to temporal variability of LSA retrievals over stable surfaces.
The quality of BPSA retrievals rely on the accurate detection of cloud and cloud shadow. Undetected cloud/shadow will generate spurious high/low values.
QF cannot correctly mark the retrieval quality. For example, Some of fill values are marked as “good”.
Validation difficulties
  Limited high quality in-situ data
  Surface heterogeneity in a pixel
  Impact of cloud contamination

## Slide 24: Future Plans
Near-term
  Collect OSA, ISA evaluation results from the Net Heat Flux team and the Cryosphere team, respectively, for a comprehensive Surface Albedo evaluation report.
  Continue monitoring the LSA data and comparisons to MODIS LSAs
  Perform the LSA validation with a global distribution of ground measurements of radiative fluxes.
  Develop algorithms of temporal filtering to reduce the impacts of undented cloud and cloud shadow
  Determine an approach of integrating BPSA and DPSA outputs
  Initial end user evaluation and feedback
Mid- to long-term
  Full evaluation of updated science algorithm and code
  Provisional status by Nov, 2013 (adjustment request: March 2014)
  Validated Version 1 status by July, 2014 (adjustment request: Nov 2014)

## Slide 25: Summary
Beta release of Suomi NPP VIIRS-SA-EDR is ready.
Validations are performed with comparisons to MODIS LSA, in-situ LSA, LSA map monitoring, evaluation of LSA temporal stability.
Continuous efforts have been put to improve the BPSA LSA retrievals. The latest LUT with BRDF as inputs is ready for implementation.
A temporal filter will be developed to reduce the impacts of undetected cloud and cloud shadow on BPSA retrievals.
Further evaluation will be conducted to better understand uncertainties of LSA products and provide comprehensive validation reports.