## Slide 1: VIIRS NCC Imagery at Beta CCR 12-0683 DR 4859
Dr. Thomas Kopp – Imagery Validation Lead
Dr. Donald Hillger – Imagery Product Lead
Mr. Ryan Williams - Imagery JAM

## Slide 2: Brief summary of NCC Imagery
The NCC Imagery EDR takes VIIRS DNB SDRs and transfers the appropriate values on as Ground Track Mercator (GTM) projection
GTM uses the nearest pixel, it does not use an average unless an isolated pixel has a bad value
Creating NCC Imagery includes two additional steps not taken for any other imagery product
  It computes an albedo for each pixel
  It mitigates solar/lunar variations across scan lines through the use of Look-Up Tables (LUTs)

## Slide 3: Typical Terminator NCC Image
Image is extreme northern Canada
  Transition from light to dark not obvious

## Slide 4: NCC Imagery Requirements
Current requirements based on the Level 1 Requirements Document (L1RD) are restricted to resolution, mapping accuracy, and latency
  Quality requirements found in the old NPOESS program are no longer present
Actually use of NCC Imagery tied to ability of a human analyst to determine his/her features of interest through Imagery
  If the operational user is not satisfied, the Imagery EDR has failed, independent of any quantitative requirements
The Imagery validation team has focused on the later in the early stages of validation

## Slide 5: General Guidelines
The two fundamental features the Imagery Cal/Val team focused on for NCC Imagery at this stage was its performance in the terminator and under lunar illumination conditions
  The terminator is where the LUTs have their greatest impact
  Nighttime visual imagery is unique to the NCC product
Other aspects were deferred to the SDR team
  Quantitative validation of resolution and latency handled by other teams
  Geolocation qualitatively addressed at this time
    Earlier issues have been resolved

## Slide 6: Beta Definition
Early release product
Initial calibration applied
Minimally validated and may still contain significant errors
Available to allow users to gain familiarity with data formats and parameters
Product is not appropriate as the basis for quantitative scientific publication studies and applications

## Slide 7: Beta Evaluation
Early release product
  NCC Imagery has not been extensively analyzed by operational users
  Imagery is not available to real-time users on a timely basis
    Neither NDE or AFWA can make Imagery available to their general set of customers in near real time as of this briefing
    Only the Navy is regularly reviewing the product in a near real time environment
  NCC only useful at night within 48 hours of the full moon
    Therefore only 5 nights out of the 29 day lunar cycle
Initial calibration of the DNB is complete
  VIIRS DNB SDRs declared “beta” in May 2012
  No software changes have yet been made to the NCC Imagery EDR

## Slide 8: Beta Evaluation
Minimally validated and may still contain significant errors
  Significant errors have been identified and are documented as Discrepancy Reports
    Fill values in the shape of triangles at corners of the Imagery
      This issue is related to the ground system and has already been mitigated
    Stray light evident on the dark side of the terminator
    Dark pixels contain fill indicating albedos are out-of-bounds
    Missing data exists in granules crossing the 105 solar angle boundary
  Examples of the three issues in work follow

## Slide 9: Stray Light
Root cause is sunlight shining into the sensor
Work in progress to mitigate through software

## Slide 10: Fill in Very Dark Pixels
Root cause unknown, likely from multiple causes
  Number of pixels affected increase as lunar illumination decreases

## Slide 11: No NCC Imagery at 105 Solar Angle
Root cause unknown
  Speculation is an adverse effect from a granule level flag indicating the entire granule is “day”
Diagonal follows the 105 solar angle

## Slide 12: Beta Evaluation
Available to allow users to gain familiarity with data formats and parameters
  NCC Imagery may be retrieved through CLASS or GRAVITE
  Both NDE and AFWA working towards real-time support
    AFWA is shipping NCC Imagery to NRL-Monterey in near real time
      Some of this Imagery appears on their NexSat web site
Product is not appropriate as the basis for quantitative scientific publication studies and applications
  NCC Imagery, in general, does not contain quantitative applications
  VIIRS DNB SDRs only at beta stage
  Also note the issues just shown

## Slide 13: Conclusion
NCC Imagery has met the beta stage based on the definitions and the evidence shown
  It exceeds the definition of beta in some cases
Remaining issues are known and at least a preliminary way ahead has been established
  Each of the four identified issues has been mitigated or is actively being resolved
NCC imagery has reached the beta stage of validation