## Slide 1: Comparison of SDR/L1B Data from OMPS and GOME-2
X. Wu1, R. Lang2, J. Zeng3, R. Munro2, M. Grotenhuis3, L. Flynn1, and C. Pan4
1: NOAA/NESDIS/STAR; 2:EUMETSAT; 3: ERT; 4: University of Maryland
EUMETSAT Meteorological Satellite Conference
Geneva, Switzerland, 23 September 2014

## Slide 2: Motivation (1/2)
The Ozone Mapper Profiler Suite (OMPS) was launched onboard the U.S. Suomi National Polar-orbiting Partnership (S-NPP) in October 2011.
  Will be a payload in future Joint Polar Satellite System (JPSS).
The second generation of the Global Ozone Monitoring Experiment (GOME-2) instruments were launched onboard the European METOP-A in October 2006 and METOP-B in September 2012.
  Will also be carried on METOP-C
Tow series of sophisticate instruments for the remote sensing of ozone, each for ~two decades.
  Nearly concurrent – unique opportunity e.g. some OMPS may overlap with three GOME-2 and vice versa.
  Interested in their long term comparison.

## Slide 3: Motivation (2/2)
Signal
Instrument
SDR, or Level 1B
EDR (Ozone, aerosol, SO2)
Instrument Performance Monitoring
EDR Validation
SDR Validation
Courtesy Google, Weng et al, Wu et al. and Pan et al.

## Slide 4: OMPS & GOME-2 Calibration
The key product for both instruments is the ratio of the back scattered UV radiance to the incoming solar radiance.
Both instruments regularly sense solar irradiance reflected from a Solar Diffuser (SD) such that instrument degradation is self-corrected, as long as the SD is stable.
  OMPS maintains SD stability with a Reference Diffuser.
  The Spectral Line Source (SLS) on GOME-2A for the same purpose did not work as expected on orbit.
OMPS has been exceptionally stable.
  Working SD has degraded slightly.
  Shortwave channels degradation became certain only recently.
GOME-2 (esp. METOP-A): up to ~10% degradation due to SD.
  Will be corrected in Level 1C.

## Slide 5: Simultaneous Nadir Overpass (SNO)
No compensation for size, shape, and orientation of FOV’s :
Scene (ozone distribution) is often sufficiently uniform.
Caution: SZA variation within the scene, esp. NP.

## Slide 6: SNO Results with METOP-A/B
Metop-A
Metop-B
Solar
Earth View
Reflectance

## Slide 7: SNO Results with METOP-A/B
Metop-A
Metop-B
Solar
Earth View
Reflectance

## Slide 8: Simultaneous Nadir Overpass (SNO)
No compensation for size, shape, and orientation of FOV’s :
Scene (ozone distribution) is often sufficiently uniform.
Caution: SZA variation within the scene, esp. NP.

## Slide 9: Time Series of SNO
Chart: Reflectance Ratio (OMPS/GOME-2)
| 40998 | 41102 | 41154 | 41256 | 41358 | 41461 | 41513 | 41564 | 41616 | 41719 | 41771
315nm | 0.87331 | 0.8636 | 0.86012 | 0.89908 | 0.86163 | 0.87719 | 0.85504 | 0.84105 | 0.85177 | 0.81951 | 0.83783
325nm | 0.85328 | 0.86371 | 0.8615 | 0.89589 | 0.86892 | 0.88261 | 0.86713 | 0.85876 | 0.85977 | 0.83987 | 0.84744
335nm | 0.87693 | 0.87999 | 0.87942 | 0.91472 | 0.8945 | 0.90391 | 0.8937 | 0.8898 | 0.88794 | 0.87154 | 0.87448
345nm | 0.8991 | 0.90456 | 0.90466 | 0.93283 | 0.92257 | 0.93252 | 0.92311 | 0.91406 | 0.90923 | 0.8987 | 0.8988
355nm | 0.93905 | 0.8995 | 0.9034 | 0.93661 | 0.92419 | 0.92996 | 0.92615 | 0.92759 | 0.91903 | 0.91064 | 0.90741
365nm | 0.92902 | 0.91188 | 0.91899 | 0.93868 | 0.93641 | 0.94333 | 0.93941 | 0.93542 | 0.92068 | 0.91775 | 0.91468
375nm | 0.87772 | 0.92546 | 0.93569 | 0.94113 | 0.94788 | 0.95776 | 0.95563 | 0.94662 | 0.92511 | 0.92934 | 0.9274
Chart: Reflectance Ratio (OMPS/GOME-2)
| 41284 | 41335 | 41386 | 41489 | 41540 | 41642 | 41694 | 41746 | 41797
315nm | 1.0283 | 1.0228 | 1.0052 | 0.98533 | 0.97517 | 0.99975 | 0.99063 | 0.97248 | 0.96871
325nm | 0.99586 | 0.98163 | 0.9805 | 0.97229 | 0.95332 | 0.98643 | 0.9627 | 0.95002 | 0.9537
335nm | 1.0016 | 0.99161 | 0.99122 | 0.98388 | 0.96518 | 0.99966 | 0.97811 | 0.96305 | 0.96449
345nm | 1.0036 | 0.996 | 1.001 | 0.99396 | 0.97291 | 1.0037 | 0.98181 | 0.96922 | 0.97139
355nm | 0.99969 | 0.99018 | 0.98928 | 0.98574 | 0.9667 | 1.0057 | 0.98132 | 0.9695 | 0.97348
365nm | 0.99671 | 0.98998 | 0.9935 | 0.98889 | 0.96597 | 0.99555 | 0.97607 | 0.96594 | 0.97269
375nm | 0.99115 | 0.98836 | 0.99888 | 0.99682 | 0.96994 | 0.99051 | 0.97395 | 0.97022 | 0.9782
NM Day 1 Solar
Stray Light Correction
Degradation rate vs. orbit life and λ.
Known events.
Unknown fluctuations.

## Slide 10: Time Series of SNO
Chart: Reflectance Ratio (OMPS/GOME-2)
| 40998 | 41102 | 41154 | 41256 | 41358 | 41461 | 41513 | 41564 | 41616 | 41719 | 41771
315nm | 0.87331 | 0.8636 | 0.86012 | 0.89908 | 0.86163 | 0.87719 | 0.85504 | 0.84105 | 0.85177 | 0.81951 | 0.83783
325nm | 0.85328 | 0.86371 | 0.8615 | 0.89589 | 0.86892 | 0.88261 | 0.86713 | 0.85876 | 0.85977 | 0.83987 | 0.84744
335nm | 0.87693 | 0.87999 | 0.87942 | 0.91472 | 0.8945 | 0.90391 | 0.8937 | 0.8898 | 0.88794 | 0.87154 | 0.87448
345nm | 0.8991 | 0.90456 | 0.90466 | 0.93283 | 0.92257 | 0.93252 | 0.92311 | 0.91406 | 0.90923 | 0.8987 | 0.8988
355nm | 0.93905 | 0.8995 | 0.9034 | 0.93661 | 0.92419 | 0.92996 | 0.92615 | 0.92759 | 0.91903 | 0.91064 | 0.90741
365nm | 0.92902 | 0.91188 | 0.91899 | 0.93868 | 0.93641 | 0.94333 | 0.93941 | 0.93542 | 0.92068 | 0.91775 | 0.91468
375nm | 0.87772 | 0.92546 | 0.93569 | 0.94113 | 0.94788 | 0.95776 | 0.95563 | 0.94662 | 0.92511 | 0.92934 | 0.9274
Chart: Reflectance Ratio (OMPS/GOME-2)
| 41284 | 41335 | 41386 | 41489 | 41540 | 41642 | 41694 | 41746 | 41797
315nm | 1.0283 | 1.0228 | 1.0052 | 0.98533 | 0.97517 | 0.99975 | 0.99063 | 0.97248 | 0.96871
325nm | 0.99586 | 0.98163 | 0.9805 | 0.97229 | 0.95332 | 0.98643 | 0.9627 | 0.95002 | 0.9537
335nm | 1.0016 | 0.99161 | 0.99122 | 0.98388 | 0.96518 | 0.99966 | 0.97811 | 0.96305 | 0.96449
345nm | 1.0036 | 0.996 | 1.001 | 0.99396 | 0.97291 | 1.0037 | 0.98181 | 0.96922 | 0.97139
355nm | 0.99969 | 0.99018 | 0.98928 | 0.98574 | 0.9667 | 1.0057 | 0.98132 | 0.9695 | 0.97348
365nm | 0.99671 | 0.98998 | 0.9935 | 0.98889 | 0.96597 | 0.99555 | 0.97607 | 0.96594 | 0.97269
375nm | 0.99115 | 0.98836 | 0.99888 | 0.99682 | 0.96994 | 0.99051 | 0.97395 | 0.97022 | 0.9782
NM Day 1 Solar
Stray Light Correction
Degradation rate vs. orbit life and λ.
Known events.
Unknown fluctuations.

## Slide 11: Chasing Orbit – Method (1/2)
Ground track of S-NPP orbit (blue) is chasing that of NOAA-19 (green)

## Slide 12: Chasing Orbit – Method (2/2)

## Slide 13: Chasing Orbit – NM
Stray Light Correction

## Slide 14: Chasing Orbit – NP
NP Day 1 Solar
Correction SAA Dark

## Slide 15: Stable Earth Target – Tropical Pacific
Assume that reflectance from clear ocean is invariant.
20S - 20N, 100W - 180W.
Plenty clear scenes.
Stable ozone content.
Low aerosols.
Use “minimum reflectance” to identify clear scenes:
Account for Raleigh scattering.
Select the reflectance in the darkest 1st percentile.

## Slide 16: Stability – method
Using spectral radiance to identify clear pixels.
Spectral reflectance with and without consideration of Rayleigh scattering variation with solar irradiance.

## Slide 17: Stability – results
OOB Stray Light Correction
Also did similar (but separately) over Libyan Desert. It seems that UV radiance is scattering limited so the underlying surface doesn’t matter. The aerosols do, however.
Day 1 Solar update

## Slide 18: Summary
Instead of calibrating one instrument using the “better” one as reference, comparison may work as long as errors (random, systematic, operational) in either instrument are not correlated.
  This is often the case and can help to understand the characteristics and operations of both, e.g., deficiencies in both OMPS and GOME-2, mostly confirm and quantify but some were unknown..
Furthermore, it would be beneficial to also compare with common references (stable earth target, other ozone instruments), in addition to direct comparison of each other.
Important to continue in long term for climate applications.
Coordinate through the newly formed UV Subgroup of the Global Space-based Inter-Calibration System (GSICS) Research Working Group (GRWG).