## Slide 1
Opportunities for using AI methods in weather forecasting at ECMWF
Alan Geer
Earth System Assimilation Section, Research Department
Thanks to: Patricia de Rosnay, Peter Dueben, Peter Bauer, Leonhard Scheck (DWD/LMU), Elias Holm, Peter Lean, Massimo Bonavita, Marcin Chrust, Robin Hogan, Mohamed Dahoui, Lars Isaksen, Stephen English, Andy Brown

## Slide 2: ECMWF’s core goal: maximising an objective function
Quality of weather forecast
1981
2019
Better
Time
Day 3
Day 5
Day 7
Day 10

## Slide 3: Data assimilation for weather forecasting Variational minimisation of a cost function to blend short forecast and new observational data
Data assimilation
Data assimilation
Data assimilation
Observations
Observations
Observations
Long forecasts
Short forecast
Short forecast
Time
09 UTC
21 UTC
09 UTC
21 UTC
4D-Variational data assimilation: Bayes theorem with Gaussian error assumption
Observations, physical forward models (radiative transfer theory)
Physical model of the atmosphere (fluid dynamics, thermodynamics, …)

## Slide 4: What can AI techniques bring?
1. Computational efficiency savings
  Replace physically-based models with more-efficient neural networks (NN)?
2. Do new things
  Satellite monitoring and quality control
  Data assimilation, observation operators, bias correction
  Learn model components
    Model physics – clouds, precipitation, turbulence, gravity wave drag, radiation
    Model error estimation
  Downstream postprocessing of the forecast
3. Replace traditional numerical weather prediction entirely?
How soon can we detect SAPHIR going wrong and apply quality control?
Bias [K]
Nov 2018
Oct 2018

## Slide 5: What can AI techniques bring?
1. Computational efficiency savings
  Replace physically-based models with more-efficient neural networks (NN)
2. Do new things
  Satellite monitoring and quality control
  Data assimilation, observation operators, bias correction
  Learn model components
    Model physics – clouds, precipitation, turbulence, gravity wave drag, radiation
    Model error estimation
  Downstream postprocessing of the forecast
3. Replace traditional numerical weather prediction entirely?

## Slide 6: Ambitious science goals, e.g. Move ensemble forecasts from the current 18 km resolution, to 5km
New science goals leading to increased cost
Computational efficiency savings or cheaper methods
Increasing supercomputer capacity

## Slide 7: 9km forecast model in data assimilation “outer loop” Operational cycle 43r3 configuration: 704 parallel processes with 6 CPUs each
0%
100%
Time: 4 mins 30 secs
Time: 0
Nonlinear forecast and compute observation equivalent
Setup
Communication
File I/O
Compute
Idle CPUs

## Slide 8: 9km forecast model in data assimilation “outer loop” Operational cycle 43r3 configuration: 704 parallel processes with 6 CPUs each
Nonlinear forecast and compute observation equivalent
Model physics | 26%
Store trajectory | 17%
Model dynamics | 12%
Coupled wave model | 12%
Others | (30%)
Observation equivalents | 1.8%
Cost breakdown by activity
Of which:
1.6% communication: moving data to observation locations
0.2% compute: observation forward models are already fast
Single column “embarrassingly parallel” compute
Communication-dominated

## Slide 9: Fast radiative transfer for observation operators – RTTOV Developed by the EUMETSAT NWP-SAF combining UK Met Office, Météo France, ECMWF and DWD
Fast approximations fitted to reference physical models, using a training dataset:
Linear regression of optical depths
    - against carefully chosen predictors
Principal components (optional)
    + improved extrapolation using Gaussian kernels
Neural networks (research)
    All-sky solar scattering radiative transfer currently uses an 8 dimensional lookup table (MFASIS, Scheck et al., 2016, JQSRT)
    Try replacing LUT with 5 layer NN, 26 nodes each
Eyre, 1991, ECMWF TM 176
Havemann et al. (2018, JQSRT)
Current work of Leonhard Scheck at DWD
10 GB
30 kB

## Slide 10: Replacing physics parametrisations in the forecast model Current work of Jakob Progsch, Christoph Angerer from NVIDIA and Peter Dueben, Robin Hogan, Peter Bauer from ECMWF
Downward shortwave (solar) radiation at the surface
Physically-based model NN trained on model
Vertically resolved heating/cooling rate profiles are also critical
  But there is not always such good emulation of radiative flux profile, particularly in vicinity of clouds

## Slide 11: Replacing physics parametrisations in the forecast model
Chevallier et al. (1999 ECMWF TM 276 ) “Use of a neural network-based longwave radiative transfer scheme at ECMWF”
  6000 profile training dataset
  7 times speedup
  Physics-aware NN designed to fit within the physical problem (inside the cloud overlap):
    2 NNs, 1 each for up and down clear-sky fluxes
    2 x N(layers) NNs for up and down cloudy fluxes
Cooling rate errors:
Stddev (NN – physical model)
Model level
Forecast errors: nearly identical with NN or physical scheme

## Slide 12: Replace the atmospheric dynamics
Dueben and Bauer (2018, GMD, https://doi.org/10.5194/gmd-11-3999-2018)
  Can NN replace the physically-based 500hPa geopotential height forecast?
  6 degree resolution single-level training
  Best results with local stencil (not global) approach
Local NN only slightly worse than a T21 (1000km resolution) forecast model
But this is the real target: TCo1279 (9km) forecast model with around 1010 state vector size

## Slide 13: What can AI techniques bring in improving efficiency?
Fast modelling:
  Traditional: linear regression, LUT and principal components
  New opportunities with ML, NN
How to do fast modelling?
  Replace the whole model
    E.g. Atmospheric profiles in → TBs / heating rates out
  Replace key components within a physically-based model
    E.g. RTTOV gas optical depths, solar reflectivity lookup table
Currently more success with “physically aware” use of traditional and ML data reduction techniques, within physical framework models
Challenge for ML: can it more directly replace physical models (e.g. fluid dynamics, radiative transfer)?

## Slide 14: What new things can we do with AI techniques?
Replace traditional weather forecasting (NWP) entirely?
Just hang on a moment – how different are data assimilation and machine learning anyway?
  AI techniques and the overlap with data assimilation have been exciting interest for years – e.g. Hsieh and Tang (1998, BAMS)
  Also see Peter Jan van Leeuwen’s talk on Wednesday: “Machine learning meets data assimilation”

## Slide 15: Machine learning (e.g. NN) Variational data assimilation
Labels |  | Observations | 
Features |  | State | 
Neural network or other learned models |  | Physical forward model | 
Objective or loss function |  | Cost function | 
Regularisation |  | Background term | 
Iterative gradient descent |  | Conjugate gradient method (e.g.) | 
Back propagation |  | Adjoint model | 
Train model and then apply it |  | Optimise state in an update-forecast cycle | 
Labels |  | Observations | 
Features |  | State | 
Neural network or other learned models |  | Physical forward model | 
Objective or loss function |  | Cost function | 
Regularisation |  | Background term | 
Iterative gradient descent |  | Conjugate gradient method (e.g.) | 
Back propagation |  | Adjoint model | 
Train model and then apply it |  | Optimise state in an update-forecast cycle | 

## Slide 16: Machine learning (e.g. NN) Variational data assimilation
Labels |  | Observations | 
Features |  | State | 
Neural network or other learned models |  | Physical forward model | 
Objective or loss function |  | Cost function | 
Regularisation |  | Background term | 
Iterative gradient descent |  | Conjugate gradient method (e.g.) | 
Back propagation |  | Adjoint model | 
Train model and then apply it |  | Optimise state in an update-forecast cycle | 
Labels |  | Observations | 
Features |  | State | 
Neural network or other learned models |  | Physical forward model | 
Objective or loss function |  | Cost function | 
Regularisation |  | Background term | 
Iterative gradient descent |  | Conjugate gradient method (e.g.) | 
Back propagation |  | Adjoint model | 
Train model and then apply it |  | Optimise state in an update-forecast cycle | 
1: Model
2: Statistical basis
3: Application

## Slide 17: Convergence
1. Model | Train or incorporate a physical (differential equation) model |  | Include NN components in physical models
2. Statistical basis | Are there more rigorously formulated Bayesian versions of machine learning? (Yes – e.g. RM Neal, “Bayesian learning for neural networks”, PhD thesis, 1995) But does Bayes approach mean the same thing in ML and DA? |  | Bayes theorem underlies data assimilation. As applied in NWP: Incorporates uncertain prior knowledge (from earlier observations and model) Constrains solutions according to physical knowledge from models Considers observation error
3. Application | Can machine learning be operated in a “continuous learning” (Bayesian update) mode? |  | Forecast model “training” is already a concept in data assimilation: “parameter estimation” Fully train a physical model (e.g. Bocquet et al., 2019, https://doi.org/10.5194/npg-2019-7: “Data assimilation as a deep learning tool to infer ODE representations of dynamical models”)
Data assimilation
Machine learning

## Slide 18: Initial goals for AI implementation within operational forecasting
Incorporate NN as an additional bias model (targeting either satellite bias or model errors) within variational data assimilation
Even if NN representations of forecast model components are not yet accurate enough to replace the physical nonlinear models, they and their back-propagation/adjoint models could replace hand-coded simplified TL and adjoint models
As a quick and efficient tool when developing new observation operators….
SSMIS channel 11 bias [K]

## Slide 19: A NN-learned observation operator: SMOS soil moisture retrievals Work for ESA by N.J. Rodrı́guez-Fernández, P. de Rosnay, J. Muñoz-Sabater, …
SMOS: Soil Moisture and Ocean Salinity satellite
  Original solution: train a NN on the L2 retrievals (so ultimately trained on a physical-based reference model)
    Single hidden layer, 5 neurons, 13 inputs
Even better:
  Train the same network using ECMWF soil moisture forecast against observed SMOS brightness temperatures
  Unbiased with respect to ECMWF forecast model
  To become operational at ECMWF with cycle 46r1, June 2019
No physically-based reference model needed!
Next step: learn inside the DA system, and so keep NN continually updated with knowledge from new observations

## Slide 20: Conclusion: What can AI techniques bring to NWP?
Replace current numerical weather prediction?
  Will fundamental computational issues in NWP also affect its AI challengers?
    Hardest inefficiencies in NWP come from communication, not compute
    Very high dimension (1010) chaotic systems
  There exists a well-understood Bayesian framework for incorporating uncertain observations, prior knowledge and physical models: data assimilation
  Very successful physical models (fluid dynamics, thermodynamics, radiative transfer)
Improve computational efficiency
  ML adds to the toolbox of fast modelling (following lookup tables, regressions, PCs ...)
  So far, judicious “physically aware” inclusion of ML seems to work better than throwing away the whole physical framework
  Areas where reduced accuracy could be outweighed by speed and convenience:
    Replace tangent-linear and adjoint models in variational data assimilation using ML models
    Ensemble forecasting
Do new things: Learn what we do not already know
  Learn model error, bias correction, sub-grid parametrisations, new observation operators
  Apply ML within the existing Bayesian NWP observe-update-forecast cycle based on data assimilation
The most important question –
How to combine DA and ML?

## Slide 21: Computational costs of operational forecasting Fractional, averaged over 2019. Taking on average 10% of the ECMWF Cray XC40 supercomputers (total 2 x 3600 nodes with 36 cores each)
4D-Var data assimilation | 12%
Ensemble 4D-Var data assimilation | 16%
Deterministic forecast to 10 days | 9%
Ensemble forecast to 15 days | 32%
Monthly forecast to 45 days, including calibration reforecasts | 26%
Others (FSOI, seasonal, …) | 5%