## Slide 1: Observations of Atmospheric Dynamics in 3D with LEO-GEO and GEO-GEO Stereo Imaging
James L. Carr1
28 February 2019
6404 IVY LANE SUITE 333 GREENBELT, MD 20770
1Carr Astronautics, 6404 Ivy Lane, Suite 333, Greenbelt, MD 20770, USA, jcarr@carrastro.com
NOAA sponsorship NA14NES4320003 (CICS, UMD)
NASA sponsorship NNG17HP01C, TO#28 (SAMDA, SSAI)
Notes: Version 10/23/2013

## Slide 2: Collaborations
NOAA Collaboration
  Jaime Daniels, Houria Madani (Carr Astro), Wayne Bresky, Jeff Key
  Focuses on GEO-GEO combinations
  In progress with preliminary results
NASA Collaboration
  Dong Wu, Michael Kelly (APL), Jie Gong
  Focuses on LEO-GEO combination
  First-year finished, second year starts March 1st
  Starting to work with JPL

## Slide 3: MISR & GOES-R
Motivation
Method
Results
Validation
MISR Special Issue of Remote Sensing:
Carr, J.L.; Wu, D.L.; Kelly, M.A.; and Gong, J., “MISR-GOES 3D Winds: Implications for Future LEO-GEO and LEO-LEO Winds”, Remote Sens. 2018, 10(12),1885; https://doi.org/10.3390/rs10121885
3D = Velocity with 3D location of Wind in the atmosphere

## Slide 4: Motivation
MISR & GOES each have different strengths and weaknesses for Wind observations
  MISR measures cross-track velocity well and altitude (parallax), but in-track velocity couples to altitude
  GOES-R measures two wind components well, but operational wind products must infer altitude from IR temperature
MISR & GOES should be better together than each working alone and therefore solve both problems.
Advanced “Image Navigation and Registration (INR)” with the new GOES-R series makes using GOES-R with MISR attractive (geo-registration better than ~200 m @ nadir).

## Slide 5: MISR & GOES-R
LEO on NASA Terra S/C
Fore & Aft-looking Cameras
  An: nadir looking
  Af, Aa: ±26.1°
  B, C, D: oblique viewing
Red Band
  275 m resolution
  360 km swaths
Winds: Zong, Davies, Muller & Diner, 2002
GOES-16 stationed at -75.2°
GOES-17 stationed at -137.2°
Advanced Baseline Imager
  Full-Disk (5, 10, 15-min. refresh)
  CONUS (5-minute refresh)
  MESO (30, 60-sec. refresh)
Red Band
  500 m resolution
NOAA Operational Winds
JPL
MISR
GOES-R
Terra
Multi-Angle
Multi-Temporal

## Slide 6: MISR Multi-Angle Imagery
MISR Red Band
(672 nm)
275 m
Track
Color Separation shows Disparities between Cameras
  In-track is Parallax + (mostly) V-wind
  Cross-track is (mostly) U-Wind
MISR Wind Challenge is the separation of Parallax from V-Wind
(R,G,B) = (Aa, An, Af)
Dt = (45s, 0, -45s)
U (East)
V (North)
SOM Projection over WGS84 Ellipsoid
(Blocks 60, 61, 62 on P024 O098797)

## Slide 7: GOES Multi-Temporal Imagery
ABI Band 2 (B02)
(640 nm)
Remapped into MISR SOM Projection
Advanced Baseline Imager (ABI)
(R,G,B) = (T0-5min, T0, T0+5min)
275m
(Native 500 m)
Color Separation shows Disparities between Frames
  Pure Atmospheric Motion
  No Parallax
T0 picked close to MISR An Time
CONUS scene used here

## Slide 8: Disparity Measurements
Time
MISR Track
GOES
MISR
Self
40x40 MISR pixel templates
8 x 8 MISR pixel sampling (2.2 km)
Normalized Cross Correlation
Subpixel resolution by Interpolation
An

## Slide 9: Disparities

## Slide 10: Wind Retrieval Model
MISR An is designated reference (n = 0)
Solve for states at each site; is a function of
  3 positions ()
  U & V winds
  (optionally W wind)
  No synchronization
Two global “Bundle Adjustment” states allow fine adjustment of MISR block to align better with GOES imagery
Nonlinear, sparse-matrix solution of order 5N+2~104 per MISR block
Minimize:
States
to looks at

## Slide 11: Residual Disparities
A Cameras + GOES-16
Disparities ~15 km
Residuals < 275m
Residuals after Solution
Block 61 on P024 O098797

## Slide 12
MISR+GOES over CONUS 2018
One Frame of 5-minute
GOES CONUS Imagery
MISR
Path 024
Jointly
Retrieved
3D-Winds
with 2.2 km
sampling
PBL
A Cameras

## Slide 13
Florence MESO 2018
Low-altitude winds
feeding in warm, moist air
One Frame of
30-Second
GOES MESO
Imagery
PBL
A Cameras

## Slide 14
MISR+GOES
Full Disk 2018
M4 (FD every
5 minutes)
Emulated
M6 (FD every
10 minutes)
Emulated
M3 (FD every
15 minutes)
N=14,366
N=7,008
N=3,772
One Frame of
M4 5-minute
GOES FD
Imagery
A Cameras

## Slide 15: Comparison to MISR Winds

## Slide 16: MISR Wind-Height Correlation
*Slope = -100 s
*Davies, Horváth, Moroney, Zhang & Zhu, 2007
Mueller, Wu, Horváth, Jovanovic, Muller, Girolamo, Garay, Diner, Moroney & Wanzong, 2017

## Slide 17: Comparison to GOES Winds

## Slide 18
Comparison with GOES IR Height Assignments
PBL
PBL
Multilayer?
Multilayer?
>> Estimated
LEO-GEO
3D-Winds
Retrieval
Uncertainty

## Slide 19: Validation: Clear-Sky Terrain
< 200 m
< 0.5 m/s
< 0.5 m/s

## Slide 20: W Winds
W-Component is observable according to the math model
Pose 1
Pose 2
Disparity
U
V
W
2 Velocity Components
Observable from each Pose
Usually W-wind in small, so we generally constrain it to zero
Interpretation as a true “wind” requires confirmation, may be
  Cloud-top growth/collapse
  Artifact of side-looks at cloud
Apparent quality improves with number of poses
2 x (3 + 2) = 10 > 6

## Slide 21: W-Component Retrievals
UV vs. UVW Retrievals
W-Component
MISR
ABCD
+ 1 GOES
Comparison with MISR A + 1 GOES

## Slide 22
Madani, H. and J. Carr, “Stereo Cloud Top Height Products for the GOES-R Era”, NOAA Satellite Conference, April 2015.
Madani, H., J. Carr, Andrew Heidinger, and Steve Wanzong, “Inter-Comparisons between Radiometric and Geometric Cloud Top Height Products”, American Geophysical Union, December 2015.
2017 Emerging Technologies Workshop
IR&D GEO-GEO Stereo Imaging
GOES-13, -14, -15
GOES-13, -15, -16
Sandy

## Slide 23
0
100 m/s
12 km
-1 km
Latitude (degrees)
Wind Speed
Wind
Height
60
40
20
0
-20
-40
-60
-140
-120
-100
-80
-60
-40
-20
Longitude (degrees)
IR&D Full Disk G-13, -16 (Test Slot)
17 September 2017 18:00Z
No Synchronization

## Slide 24: STAR Study
NOAA can do parallax 3D-Winds NOW
Objective of our present work is to prove this in a way that has a path into operations to provide alternative height assignments for DMWs
Validations/comparisons will quantify the quality of parallax heights
  Comparison with IR height assignments
  MISR-GOES winds
  Rawinsondes and aircraft wind in situ measurement
Operational Configuration
Configuration from our IR&D Study
No synchronization
Trade-off between vertical resolution and coverage

## Slide 25: STAR Study Methodology
Time
G-17 Remapped
into G-16
Fixed Grid
G-16
in the G-16
Fixed Grid
Remap G-17 into G-16 fixed grid
Match each triplet using operational winds matching & clustering algorithm
Ingest matches into MISR/GOES-heritage retrieval model
Use MISR/GOES-heritage matching for ground-point validation
Can Mix CONUS/MESO/FD

## Slide 26
CONUS Retrievals with GOES-16, -17 (Test Slot)
B02
PRELIMINARY
CONUS-CONUS
Matches from NOAA code

## Slide 27: B02 CONUS Validations
MISR + GOES
Ground Retrievals
PRELIMINARY

## Slide 28: IR Full Disk G-16, -17 (W Slot)
PRELIMINARY
FD-FD

## Slide 29: IR Ground Retrievals
We see less ground with this band than with Band 2
2.55 % of good retrievals are ground for Band 14
11.25% of good retrievals are ground for Band 2
PRELIMINARY

## Slide 30: Full Disk WV 3D-Winds
Mean=10212 m
Mean=9540 m
Mean=859 m
Just for Fun!
PRELIMINARY
Did we retrieve the height? TBD
FD-FD

## Slide 31
B08
B09
PRELIMINARY
WV 3D-Wind Comparisons with DMW Products

## Slide 32: The Future
LEO-GEO Constellations
LEO-LEO Leader-Follower
Cubesat Deployments
International Partners
Hosted Payloads