## Slide 1
Attributes of Earth System Variables for Comparing Observing System Performances to Application Requirements
ASPEN Team
2023 September 18
Ross N Hoffman
Cooperative Institute for Satellite Earth System Studies (CISESS) College Park MD

## Slide 2: Summary
To determine how well an observing system satisfies the requirements of an applications we need
A common description of the variables of interest,
The attributes of those variables in order to characterize both the observing system performances and the application requirements, and
Metrics to measure the degree of satisfaction.
At the June 12 SAT meeting, we discussed the variables in depth and looked briefly at the attributes. Here, we will consider the attributes in depth and touch on the comparison metrics.

## Slide 3: Attributes

## Slide 4: Motivation
The goal is for independent groups to describe observing system performances or application requirements in a way that can be fairly compared.
For example, are there different definitions of “flood” in use by the algorithm developer, modeling, nowcasting, disaster monitoring, and climate communities?
  Similar questions occur for other variables (e.g., cloud, snow cover, fire).
If these definitions cannot be agreed upon, collaboration between diverse communities will be hampered.

## Slide 5: Status
Still open for discussion
We are sharing a google document describing the attributes in detail. Please feel free to offer comments and suggestions.
An ASPEN revision is underway to test the viability of the variables and attributes we’ve presented. We expect actual use will lead to refinement.
Beyond ASPEN, the usefulness of these descriptions of the Earth System variables and their attributes will depend on the buy-in from the different communities.
In this context getting to agreement is more important than getting to perfection.

## Slide 6: Things to Consider
Independence of observations
Exclusions
What should be included in biases
Attribute definitions can depend on the variable
Subsets
Error attributes

## Slide 7: Independence of observations
Many attributes relate to the number of observations provided or required.
To allow for fair comparisons, the number of observations in these definitions of attributes are an effective number that represents the independent pieces of information in the data set (observed or required) in the sense that if the observation were thinned to the effective number, the remaining observation errors would not be correlated in time or space.
  For example, algorithms to convert radiances to temperature profiles can retrieve temperature on any vertical grid, but the effective degrees of freedom in the vertical is fixed by the instrument characteristics.
  For example, NWP grids are fine, but requirements for data are coarser.

## Slide 8: Exclusions
Sources of exclusion include cloud, surface types, solar zenith angle, RFI
Exclusions potentially affect many attributes of observations
Instead, we include an attribute called exclusion factor
All other estimated attributes ignore exclusion factors
During comparisons the exclusion factor can be applied to different attributes (Revisit Time, Spatial Density, or Precision) depending on the applications being considered

## Slide 9: Accuracy and mean errors (AKA biases)
In most cases simple biases are removed by the data producer.
For example, for retrieved temperature profiles any bias that depends on time of day or altitude or latitude should be removed.
Some of the biases that remain are what might be call geophysical biases.
That is, algorithms leave out some things (or assume values for some properties) and these effectively result in errors.
This results in correlated errors because those things (geophysical variables) that are left out have long space and time scales.
These geophysical biases (or algorithmic biases) are hard to estimate and hard for any analysis method to remove.
For many applications it is vitally important that these biases be small.
The RMS of these geophysical biases should be included when estimating observing system accuracy.

## Slide 10: Variable definitions and attributes
Any attribute definition might be modified for a particular variable
  This modification should be included in the variable definition
  This flexibility is fine as long as everyone interested in a particular variable accepts these modifications.
We are using this leeway for example to include space weather sensors and applications. Some variable definitions include
  Spectral units (e.g., energy in MeV)
  Vertical location reference (e.g., relative to the center of the Sun)
  Spatial units (e.g., arcsec for solar imagery)

## Slide 11: Variable definitions and attributes 2
Variable definitions also include
  The type of geophysical variable (scalar, 2D vector, 3D vector, vertical flux, 2D flux, 3D flux),
  Where defined in the vertical (surface, 2m, 10m, TOA)
  The representation for 2D and 3D variables (e.g., winds, currents, fluxes) in terms of (speed, direction) or components

## Slide 12: Subsets
Based on experience we introduce subsets
Some variables are subsetted by vertical level (2m, BL, troposphere, stratosphere, ….)
Precision is subsetted by (clear/cloudy) and (land/sea)
Revisit Time is subsetted by three latitude zones

## Slide 13: Estimating error attributes
Tricky, because we don’t know the truth
But we do it all the time, using many different approaches
If we want fair comparisons, we must agree on how we make these estimates
  Or make adjustments to account for differences between the method used and some ideal method
For this effort only specify an ideal method (textbook statistics and a large representative sample) and allow for possible modifications for specific variables
When comparing the precision of variables with Angular and Spectral Resolution or a Classification Scheme, if the observing system provides more degrees of freedom than the application requires, the observed data might be reprocessed (averaged) to the application’s resolution, which should reduce random errors

## Slide 14: Attributes Types
Data Quality
Temporal
Spatial
Vertical
Angular and Spectral
Data Type
System

## Slide 15: Data Quality Attributes

## Slide 16: Validity range
E.g., Legacy scatterometers observe winds in the range [2,30] m/s.
Validity range low is the lowest value that can be observed.
Validity range low is equivalent to noise floor.
Validity range high is the highest value that can be observed.
Validity range high is equivalent to saturation level.

## Slide 17: Temporal Attributes

## Slide 18: Revisit Time vs. Refresh Rate
  Definitions
    Revisit Time :: Typical time (hr) between observations at a location.
    Refresh Rate :: Number of times a location is observed in a day (obs/day)
    Since these are reciprocals, the arithmetic mean of refresh rate is equivalent to the harmonic mean of the revisit time
  Consider 6 locations
    There are a total of 42 observations in a day for an average refresh rate of 7 obs/day, equivalent to a revisit time of 3.43 hr (24/7).
    But the average revisit time is 4.9 which would imply 29.4 observations in a day which is inconsistent with reality
    This non-conservation of total observations is why averaging revisit time is not correct

## Slide 19: Revisit Time vs. Refresh Rate
  Definitions
    Revisit Time :: Typical time (hr) between observations at a location.
    Refresh Rate :: Number of times a location is observed in a day (obs/day)
    Since these are reciprocals, the arithmetic mean of refresh rate is equivalent to the harmonic mean of the revisit time
  Consider 6 locations
    There are a total of 42 observations in a day for an average refresh rate of 7 obs/day, equivalent to a revisit time of 3.43 hr (24/7).
    But the average revisit time is 4.9 which would imply 29.4 observations in a day which is inconsistent with reality
    This non-conservation of total observations is why averaging revisit time is not correct
  Revisit time in a region is properly defined as the harmonic mean of the individual revisit times in the region.

## Slide 20: Spatial Attributes

## Slide 21: Spatial coverage
Spatial (usually geographic) application domain or region observed (e.g., CONUS)
Space weather regions observed such as “3–22 Rsun @ L4”
For comparison the regions and domains are arbitrary as long as we know how to specify the overlap.
    The performance score is the amount of overlap of the application domain by the observing system domain.

## Slide 22: Geographic overlaps
Sensor Region
GEO observations
Tropical application
Overlap = 32%
Overlap = 0%
Polar observations
Tropical application
Application Domain

## Slide 23: Spatial density
The average number of observations in a 100 km x 100 km square area
  For satellite data this is average across the swath
    Across a single swath, does not account for overlapping swaths near poles.
  For radiosondes this is number of radiosondes in 12 h period divided by the the area covered by land (in units of 100 km x 100 km)

## Slide 24: Spatial resolution
Typical length of the GIFOV (ground-projected instantaneous field of view)
Note: SPRWG says horizontal resolution is the spacing between observations.

## Slide 25: Vertical Attributes

## Slide 26: Vertical extent overlap
Vertical extent will be scored by overlap but is still coded as two attributes: [Vertical Extent Bottom, Vertical Extent Top]
Water vapor
IR observations
GNWP application
Overlap = fraction of blue app box overlapped by green obs box
Temperature
GNSS observations
GNWP application
1000
900
100
1000
300
100
50
Pressure (hPa)
Sensor
Application
Notes: Also applies to spectral range

## Slide 27: Vertical extent overlap
Vertical extent will be scored by overlap but is still coded as two attributes: [Vertical Extent Bottom, Vertical Extent Top]
Water vapor
IR observations
GNWP application
Temperature
GNSS observations
GNWP application
1000
900
100
1000
300
100
50
Pressure (hPa)
Sensor
Application
Overlap = [min(Smax, Amax) - max(Smin, Amin)]/[Amax-Amin)
Overlap = 78%
Overlap = 88%
Notes: Also applies to spectral range

## Slide 28: Angular and Spectral Attributes

## Slide 29: Spectral range and resolution
Some variables have a distribution over some descriptive parameter. Typically, this will be a frequency, energy, or size spectra. Examples include
  Solar EUV Irradiance (wavelength, nm)
  Drop size (diameter, mm)
  Solar Energetic Particles (energy, MeV)
Spectral attributes are given in terms of spectral units (e.g., energy, MeV)
Spectral range will be scored by overlap like vertical extent.

## Slide 30: Data Type Attributes

## Slide 31: System Attributes

## Slide 32: Prior data
Is prior data used/allowed for this variable.
  E.g., use of an NWP background field for some ABI products
Some models may not allow prior data use in variables that are updated by DA but would allow prior data for some variables that provide boundary conditions, e.g., soil moisture, SST.

## Slide 33: Robustness
Number of sources making this observation
  Always 1 for a single sensor.
Robustness includes many factors; this definition includes only redundancy only. Resiliency, i.e., how quickly can a loss of capability be replaced is not included here.

## Slide 34: Data latency
Time from ‘image taken’ to ready to be used by applications.
  Note that this includes processing time.
We include two data latencies: direct readout and normal transmission.
Still open for discussion.

## Slide 35: Long term stability
There are two attributes
  Long term changes in accuracy (drift)
  Long term changes in precision (noise)
Units could be different for different variables
  Usually, the units will be the same as for error standard deviation, but per decade.

## Slide 36: Normalizations
Min-Max
Linear Overlap
LUT Overlap
Logical

## Slide 37: Min-Max Scoring
The performance score for many attributes is the observed performance normalized by the minimum and maximum useful requirements.
Precision
Score
SST | NWP | Ocean
Requirements | [1, 4] | [0.1, 3]
ABI sd=2.00 | 0.67 | 0.34
VIIRS sd=0.20 | 1.00 | 0.97

## Slide 38: Overlap calculations
The performance score for geographic coverage is calculated as the fraction of the required domain that is covered (overlapped) by the observed region.
  This requires GIS calculations from shape files for the regions. The results are stored in a LUT.
  Other LUTs include time of day and categories
A similar linear overlap approach can be applied in one-dimension to attributes where a range (min, max) is required or observed
  Attributes with a range: vertical extent, validity range, spectral range, continuity
Logical attributes have a very simple LUT equivalent to the logical AND

## Slide 39: Time of day overlap
 | Day | Night | Day/Night
Day | 1 | 0 | 0.5
Night | 0 | 1 | 0.5
Day/Night | 1 | 1 | 1
Sensor
Application

## Slide 40: end