## Slide 1: Assessment of Users Observational Needs SAT Consolidation of Requirements Ranges and Priorities for Global NWP
Stacy Bunin
Sid Boukabara, Frank Gallagher (co-chairs)
October 4, 2021

## Slide 2: Overview
Collection of quantitative assessment of priorities and requirements ranges for observational needs specific to application of Global NWP
Collected by SAT subcommittee on Global NWP
Reviewed by General SAT discussion
Purpose is to consolidate requirements ranges and priorities from users’ perspective
Specific to current Global NWP needs
Contributors include SAT participants from the NOAA users, non-NOAA federal agency users, research community, academia, and private sector
The ultimate goal is to use these observational needs as inputs to assess the actual relevant requirements that NOAA adopt for the architecture design and evolution

## Slide 3: Content
Geophysical Capability Priorities
Individual Geophysical Capability Attributes, Ranges, and Priorities
  Temperature Profiles
  Atmospheric Wind Speed Profiles
  Surface Pressure
  Relative Humidity Profiles
  Sea Ice Concentration
  Snow Cover
  Sea Surface Temperature
  Cloud Top Temperature
  Cloud Liquid Water Path
  Normalized Difference Vegetation Index
  Soil Moisture
  Snow Water Equivalent

## Slide 4: Observational Needs for Application: Global NWP
Geophysical Capability | Priority
Temperature Profiles | 1.0
Atmospheric Wind Speed Profiles | 1.0
Surface Pressure | 0.8
Relative Humidity Profiles | 0.6
Sea Ice Concentration | 0.2
Snow Cover | 0.2
SST | 0.2
Geophysical Capability Priorities

## Slide 5: Observational Needs for Application: Global NWP
Geophysical Capability | Priority
Cloud Top Temperature | 0.05
Cloud Liquid Water Path | 0.05
Normalized Difference Vegetation Index | 0.05
Soil Moisture | 0.05
Snow Water Equivalent | 0.05
Others? | 0.05
Geophysical Capability Priorities

## Slide 6: Observational Needs for Application: Global NWP Geophysical Capability: Temperature (K)
 | Attribute Ranges | Priority
Geographic Coverage | Global | 1
Horizontal Density ((100 km)-2) | NA | 0
Horizontal Resolution (km) | [100,50,1] | 0.1
Vertical Resolution (d.o.f.) for 0-10 km layer | [5,10,33] | 1
Vertical Extent Bottom (km) | NA | 0
Vertical Extent Top (km) | NA | 0
Temporal Refresh (h) | [12,3,0.5] | 1
Uncertainty (Error Standard Deviation) (K) | [2,1,0.5] | 1
Robustness | NA | 0
Latency (h) | [3,1,0.25] | 0.5
Attributes Ranges and Priorities
*Attribute Ranges: (Minimally Useful, Expected, Maximum Effectiveness)

## Slide 7: Observational Needs for Application: Global NWP Geophysical Capability: Atmospheric Wind Speed (m/s)
 | Attribute Ranges | Priority
Geographic Coverage | Global | 1
Horizontal Density ((100 km)-2) | NA | 0
Horizontal Resolution (km) | [100,50,1] | 1
Vertical Resolution (d.o.f.) | [3,10,20] | 1
Vertical Extent Bottom (km) | NA | 0
Vertical Extent Top (km) | NA | 0
Temporal Refresh (h) | [12,3,0.5] | 1
Uncertainty (Error Standard Deviation) (%) Uncertainty (Error Standard Deviation) (m/s) | [20,10,5] [4,2,1] | 1
Robustness | NA | 0
Latency (h) | [3,1,0.25] | 1
Attributes Ranges and Priorities
*Attribute Ranges: (Minimally Useful, Expected, Maximum Effectiveness)

## Slide 8: Observational Needs for Application: Global NWP Geophysical Capability: Surface Pressure (hPa)
 | Attribute Ranges | Priority
Geographic Coverage | Global | 1
Horizontal Density ((100 km)-2) | NA | 0
Horizontal Resolution (km) | [100,50,1] | 1
Vertical Resolution (d.o.f.) | NA | 0
Vertical Extent Bottom (km) | NA | 0
Vertical Extent Top (km) | NA | 0
Temporal Refresh (h) | [12,6,1] | 1
Uncertainty (Error Standard Deviation) (hPa) | [1,1,0.5] | 1
Robustness | NA | 0
Latency (h) | [12,6,1] | 1
Attributes Ranges and Priorities
*Attribute Ranges: (Minimally Useful, Expected, Maximum Effectiveness)

## Slide 9: Observational Needs for Application: Global NWP Geophysical Capability: Relative Humidity (%)
 | Attribute Ranges | Priority
Geographic Coverage | Global | 1
Horizontal Density ((100 km)-2) | NA | 0
Horizontal Resolution (km) | [100,50,1] | 1
Vertical Resolution (d.o.f.) | [2,10,33] | 1
Vertical Extent Bottom (km) | NA | 0
Vertical Extent Top (km) | NA | 0
Temporal Refresh (h) | [12,3,0.5] | 1
Uncertainty (Error Standard Deviation) (%) | [15,10,5] | 1
Robustness | NA | 0
Latency (h) | [3,1,0.25] | 1
Attributes Ranges and Priorities
*Attribute Ranges: (Minimally Useful, Expected, Maximum Effectiveness)

## Slide 10: Observational Needs for Application: Global NWP Geophysical Capability: Sea Ice Concentration (%)
 | Attribute Ranges | Priority
Geographic Coverage | Global | 1
Horizontal Density ((100 km)-2) | NA | 0
Horizontal Resolution (km) | [100,50,1] | 1
Vertical Resolution (d.o.f.) | NA | 0
Vertical Extent Bottom (km) | NA | 0
Vertical Extent Top (km) | NA | 0
Temporal Refresh (h) | [12,6,3] | 1
Uncertainty (Error Standard Deviation) (%) | [25,15,10] | 1
Robustness | NA | 0
Latency (h) | [120,24,3] | 1
Attributes Ranges and Priorities
*Attribute Ranges: (Minimally Useful, Expected, Maximum Effectiveness)

## Slide 11: Observational Needs for Application: Global NWP Geophysical Capability: Snow Cover (%)
 | Attribute Ranges | Priority
Geographic Coverage | Global | 1
Horizontal Density ((100 km)-2) | NA | 0
Horizontal Resolution (km) | [100,50,1] | 1
Vertical Resolution (d.o.f.) | NA | 0
Vertical Extent Bottom (km) | NA | 0
Vertical Extent Top (km) | NA | 0
Temporal Refresh (h) | [12,6,3] | 1
Uncertainty (Error Standard Deviation) (%) | [25,10,5] | 1
Robustness | NA | 0
Latency (h) | [120,24,3] | 1
Attributes Ranges and Priorities
*Attribute Ranges: (Minimally Useful, Expected, Maximum Effectiveness)

## Slide 12: Observational Needs for Application: Global NWP Geophysical Capability: Sea Surface Temperature (K)
 | Attribute Ranges | Priority
Geographic Coverage | Global | 1
Horizontal Density ((100 km)-2) | NA | 0
Horizontal Resolution (km) | [100,50,1] | 1
Vertical Resolution (d.o.f.) | NA | 0
Vertical Extent Bottom (km) | NA | 0
Vertical Extent Top (km) | NA | 0
Temporal Refresh (h) | [12,6,3] | 1
Uncertainty (Error Standard Deviation) (K) | [4,2,1] | 1
Robustness | NA | 0
Latency (h) | [120,24,3] | 1
Attributes Ranges and Priorities
*Attribute Ranges: (Minimally Useful, Expected, Maximum Effectiveness)

## Slide 13: Observational Needs for Application: Global NWP Geophysical Capability: Cloud Top Temperature (K)
 | Attribute Ranges | Priority
Geographic Coverage | Global | 1
Horizontal Density ((100 km)-2) | NA | 0
Horizontal Resolution (km) | [100,50,1] | 1
Vertical Resolution (d.o.f.) | [0,3,8] | 1
Vertical Extent Bottom (km) | NA | 0
Vertical Extent Top (km) | NA | 0
Temporal Refresh (h) | [12,6,3] | 1
Uncertainty (Error Standard Deviation) (K) | [10,5,1] | 1
Robustness | NA | 0
Latency (h) | [3,1,0.25] | 1
Attributes Ranges and Priorities
*Attribute Ranges: (Minimally Useful, Expected, Maximum Effectiveness)

## Slide 14: Observational Needs for Application: Global NWP Geophysical Capability: Cloud Liquid Water Path (g/m2)
 | Attribute Ranges | Priority
Geographic Coverage | Global | 1
Horizontal Density ((100 km)-2) | NA | 0
Horizontal Resolution (km) | [100,50,1] | 1
Vertical Resolution (d.o.f.) | [0,3,8] | 1
Vertical Extent Bottom (km) | NA | 0
Vertical Extent Top (km) | NA | 0
Temporal Refresh (h) | [12,6,3] | 1
Uncertainty (Error Standard Deviation) (g/m2) | [10,5,2] | 1
Robustness | NA | 0
Latency (h) | [3,1,0.25] | 1
Attributes Ranges and Priorities
*Attribute Ranges: (Minimally Useful, Expected, Maximum Effectiveness)

## Slide 15: Observational Needs for Application: Global NWP Geophysical Capability: Normalized Difference Vegetation Index (unitless)
 | Attribute Ranges | Priority
Geographic Coverage | Global | 1
Horizontal Density ((100 km)-2) | NA | 0
Horizontal Resolution (km) | [100,50,1] | 1
Vertical Resolution (d.o.f.) | NA | 0
Vertical Extent Bottom (km) | NA | 0
Vertical Extent Top (km) | NA | 0
Temporal Refresh (h) | [12,6,3] | 1
Uncertainty (Error Standard Deviation) (unitless) | [0.25,0.15,0.1] | 1
Robustness | NA | 0
Latency (h) | [120,24,3] | 1
Attributes Ranges and Priorities
*Attribute Ranges: (Minimally Useful, Expected, Maximum Effectiveness)

## Slide 16: Observational Needs for Application: Global NWP Geophysical Capability: Soil Moisture (m3/m3)
 | Attribute Ranges | Priority
Geographic Coverage | Global | 1
Horizontal Density ((100 km)-2) | NA | 0
Horizontal Resolution (km) | [100,50,1] | 1
Vertical Resolution (d.o.f.) | NA | 1
Vertical Extent Bottom (km) | NA | 0
Vertical Extent Top (km) | NA | 0
Temporal Refresh (h) | [12,6,3] | 1
Uncertainty (Error Standard Deviation) (m3/m3) | [0.2,0.1,0.05] | 1
Robustness | NA | 0
Latency (h) | [120,24,3] | 1
Attributes Ranges and Priorities
*Attribute Ranges: (Minimally Useful, Expected, Maximum Effectiveness)

## Slide 17: Observational Needs for Application: Global NWP Geophysical Capability: Snow Water Equivalent (cm)
 | Attribute Ranges | Priority
Geographic Coverage | Global | 1
Horizontal Density ((100 km)-2) | NA | 0
Horizontal Resolution (km) | [100,50,1] | 1
Vertical Resolution (d.o.f.) | NA | 0
Vertical Extent Bottom (km) | NA | 0
Vertical Extent Top (km) | NA | 0
Temporal Refresh (h) | [12,6,3] | 1
Uncertainty (Error Standard Deviation) (cm) | [8,4,2] | 1
Robustness | NA | 0
Latency (h) | [120,24,3] | 1
Attributes Ranges and Priorities
*Attribute Ranges: (Minimally Useful, Expected, Maximum Effectiveness)