## Slide 1: Using Neural Networks as Model Physics Components in Numerical Weather Prediction
V. Krasnopolsky1 and A. Belochitski2
1NWS/NCEP/EMC, 2IMSG at NCEP/EMC
Vladimir.Krasnopolsky@noaa.gov
Alexei.A.Belochitski@noaa.gov
2-nd NOAA AI Workshop, Dec 3, 2020

## Slide 2: Outline
NN emulation for Full Suite of Model Physics
Stability and Robustness
Conclusions

## Slide 3: GFS v.16 Structure
Dycore
Atmospheric Physics
RRTMG LW Radiation,
RRTMG SW Radiation,
Planetary BL,
Orographic and convective
gravity wave drag,
Deep convection,
Shallow convection,
Microphysics,
CO2(t), trace gases,
Aerosols (tropo- and stratospheric),
O3 and H2O photochemistry
Noah Land Model
Suite of Model Physics
U
V
T
Sh
Clw
O3
GFS
NN
506 Inputs
304 Outputs
250 Hidden Neurons in one hidden layer
3 times faster
Training: Data simulated by 23 10-day GFS v.16 C96L64 forecasts, uniformly covering entire 2018

## Slide 4: NN Inputs and Outputs
NN Input | NN Input # | Layers | NN Input | NN Input # | Layers
 | 1 | - | Surface Pressure | 137 | -
 | 2 | - | U-wind | 138 : 201 | 1 : 64
 | 3 | - | V-wind | 202 : 265 | 1 : 64
 | 4 | - | Vertical velocity | 266 : 329 | 1 : 64
Latitude | 5 | - | Temperature | 330 : 393 | 1 : 64
cos(Longitude) | 6 | - | Specific humidity | 394 : 430 | 1 : 37
sin(Longitude) | 7 | - | Total cond. mix. ratio | 431 : 473 | 1 : 43
cos(Zenith Angle) | 8 | - | Ozone mixing ratio | 474 : 505 | 33 : 64
Layer geop. height | 9 : 72 | 1 : 64 | Solar constant | 506 | -
Layer pressure | 73 : 136 | 1 : 64 |  |  | 
NN Output | NN Output # | Layers | NN Output | NN Output # | Layers
U-wind increment | 1 : 64 | 1 : 64 | Specific humidity incr. | 193 : 229 | 1: 37
V-wind increment | 65 : 128 | 1 : 64 | Total cond. m. r. incr. | 230 : 272 | 1 : 43
Temperature incr. | 129 : 192 | 1 : 64 | Ozone mix ratio incr. | 273 : 304 | 33 : 64
NN Input | NN Input # | Layers | NN Input | NN Input # | Layers
 | 1 | - | Surface Pressure | 137 | -
 | 2 | - | U-wind | 138 : 201 | 1 : 64
 | 3 | - | V-wind | 202 : 265 | 1 : 64
 | 4 | - | Vertical velocity | 266 : 329 | 1 : 64
Latitude | 5 | - | Temperature | 330 : 393 | 1 : 64
cos(Longitude) | 6 | - | Specific humidity | 394 : 430 | 1 : 37
sin(Longitude) | 7 | - | Total cond. mix. ratio | 431 : 473 | 1 : 43
cos(Zenith Angle) | 8 | - | Ozone mixing ratio | 474 : 505 | 33 : 64
Layer geop. height | 9 : 72 | 1 : 64 | Solar constant | 506 | -
Layer pressure | 73 : 136 | 1 : 64 |  |  | 
NN Output | NN Output # | Layers | NN Output | NN Output # | Layers
U-wind increment | 1 : 64 | 1 : 64 | Specific humidity incr. | 193 : 229 | 1: 37
V-wind increment | 65 : 128 | 1 : 64 | Total cond. m. r. incr. | 230 : 272 | 1 : 43
Temperature incr. | 129 : 192 | 1 : 64 | Ozone mix ratio incr. | 273 : 304 | 33 : 64

## Slide 5: 24 10-day forecasts (zonal means) - 1
Bias = 9.10-6 m/s
Bias = -2.10-3 K
Bias = 8.10-5 m/s

## Slide 6: 24 10-day forecasts (zonal means) - 2
Bias = 4.10-4 g/kg
Bias = 1.10-10 g/kg
Bias = 6.10-6 g/kg

## Slide 7: Evolution of Biases with Time
Forecast time
Forecast time

## Slide 8: Evolution of Biases with Time
Forecast time
Forecast time

## Slide 9: Validation of NN Model Physics
24 10-day forecasts over 2018, no signs of instability
Control run is reproduced with high accuracy
One-year continuous NN run, no signs of instability
Run NN in GFS C384L64 (trained on C96L64), no signs of instability

## Slide 10: NN Stability
General issues
  Model physics and individual parameterizations are mappings
  SNNs are generic & universal tool for approximating continuous and almost continuous mappings (Hornik 1991, 1993, Vapnik 2019)

## Slide 11: NN Complexity and Nonlinearity
Complexity and nonlinearity of approximating/emulating NN should not exceed the complexity and nonlinearity of the mapping to be approximated
  SNN vs. DNN
    SNN complexity =>
    DNN complexity =>
    SNN nonlinearity =>
    DNN nonlinearity =>
    DNN: complexity and nonlinearity increase very quickly with adding new hidden layers
    It is more difficult to control complexity and nonlinearity (overfitting and generalization) of DNN

## Slide 12: Activation Function (AF)
Choice of activation function may affect stability of NN
  If use of AFs that are not continuously differentiable (e.g., ReLU):
    May cause problems with gradient-based optimization
    Your NN emulation is not continuously differentiable
  When the range of the AF is finite, gradient-based training methods tend to be more stable
  When AF approximates identity near the origin, i.e.,
  , weights are recommended to be initialized with small random values.
  Old fashioned sigmoid and tanh fulfill all these conditions
Chart: ReLU
| -1 | 0 | 1
Series 1 | 0 | 0 | 1
Series 2
Series 3

## Slide 13: Training Set (TS)
TS preparation may affect stability of NN
  Amount of data:
    > , therefore >
    > and >
  Representativeness of data:
    Annual cycle
    Diurnal cycle
    Extreme events
  Data preprocessing:
    Proper sampling (e.g., polar areas are overrepresented in lat x lon grid)
    Proper purging and normalization of inputs and outputs (e.g., removing constants)

## Slide 14: Additional issues that may lead to NN instability
When learn a new NN parameterization for GCM from the data simulated by higher resolution model (e.g., CRM)
  Projecting: removing CRM variables that are not present in GCM
  Projecting introduces stochasticity in the training set
  ML/NN parameterization/mapping becomes stochastic and should be treated as such; otherwise NN may become unstable

## Slide 15: Conclusions
NN, when properly trained, provides an accurate and stable emulation of the full suite of the model physics in a state-of-the-art GFS
Transfer of knowledge should be performed accurately to produce stable NNs:
  DNNs are sensitive tools, require careful use
  Choice of activation function may affect NN stability
  Preparation of data sets is important for NN stability
  Stochasticity should be treated properly