## Slide 1
Modeling and Data Assimilation for UFS Applications
JPSS/GOES-R Proving Ground Risk Reduction Summit, 24 February 2020
Vijay Tallapragada
NOAA/NWS/NCEP/EMC

## Slide 2
NPS Transitioning to UFS Applications
Conceptual UFS applications in production covering all NPS applications.
Components of UFS are configured to develop distinct applications while maintaining the dependencies between the applications and products

## Slide 3
Timelines for transitioning NPS to UFS Applications (planned)
WCOSS Moratorium

## Slide 4: Recent and Planned Upgrades to the GFS
GFSv15.1 (June 2019)
  Initial implementation of FV3-based GFS
  Increase analysis increment & ensemble resolution
  No DFI
GFSv15.2 (November 2019)
  Observation changes: GOES-17 AMVs, KOMPSAT-5 GPS, METOP-C AMSU-A and MHS
  NSST Updates
GFSv15.3 (TBD)
  Observation changes: COSMIC-2,
METOP-C GRAS and IASI
GFSv16 (Early 2021)
  GSI-based Hybrid 4DEnVar
  127 Layers, ~80km model top
  Updated physics
  Modulated-ensemble LETKF (model space localization)
  4D-IAU
  Correlated observation errors
  VarQC re-design
  LDAS

## Slide 5: GFSv16 Data Assimilation Upgrades
The GFSv16 will move from 64 layers to 127 layers, raising the model top from 55 km to 80 km.
4D Incremental Analysis Update (IAU)
Replace EnSRF with LETKF (including model space localization and linearized obs operator)
Intra-channel correlated observation errors for radiances
Additional channels (AMSU-A ch14 and ATMS ch15, clear-sky radiances from Meteosat 8 (SEVIRI), Himawari 8 (AHI), GOES-16 ABI)
Variational Quality Control update
New observations
“GLDAS”
Reduced humidity increments in stratosphere
Improved NSST

## Slide 6: UFS-HAFS Strategic Roadmap

## Slide 7: Data Assimilation for Hurricane Models
 |  |  |  | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2020+
 | GSI-based DA |  |  |  |  |  |  |  |  |  |  |  |  | 
 | GSI hybrid |  |  |  |  |  |  |  |  |  |  |  |  | 
 | P3 Doppler velocity |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Dropsondes (partial) |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Global Hawk dropsondes |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Warm-start HWRF ensemble |  |  |  |  |  |  |  |  |  |  |  |  | 
 | SLP from TCVitals |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Satellite radiances/winds (D03) |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Flight-level obs. |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Fully-cycled DA (EnKF/GSI) |  |  |  |  |  |  |  |  |  |  |  |  | 
 | SFMR |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Dropsondes (all with drift) |  |  |  |  |  |  |  |  |  |  |  |  | 
 | G-IV Doppler velocity |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Stochastic physics (DA) |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Spectral filter for increments |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Dynamic obs. errors for recon |  |  |  |  |  |  |  |  |  |  |  |  | 
 | WSR-88D Doppler velocity |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Clearsky radiance data (more channels) |  |  |  |  |  |  |  |  |  |  |  |  | 
 | All sky radiance data (inner core) |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 8
GFS
GEFS
Global (10-15 km, 4-24/day)
RRFS
WoFS
CONUS/OCONUS
CAM (3 km, 2-24/day)
Sub-CONUS
CRM (1 km, on-demand)
Long Term
Rapid Refresh
Forecast System
Warn on Forecast
System
GFS/GEFS
to subsume
RAP/NAM/SREF
RRFS to subsume
HRRR/NAMnest/HREF
What is the RRFS and how do we get there?
*Material courtesy of C. Alexander
UFS: Simplification of Regional Model Production Suite

## Slide 9: Ongoing Radiance DA Development
Hourly assimilation of radiances
  Same data as GFS
Using radiance data through Regional ATOVS Retransmission Service (RARS) to reduce the data latency
Bias corrections for all satellite instruments are estimated within the regional system
Coldstart from GFS
Hourly hybrid 3DEnVar assimilation
Using global EnKF members
60 hr 3 km forecast
6 hour forecast at 3 km
GOES-16 O-Bs
GOES-16 O-Bs and O-As with bias correction
*Material courtesy of X. Zhang