## Slide 1: An ESPA-Grande-compatible free-flyer wind lidar mission design for aerosol and/or molecular winds
Ball Aerospace, stucker@ball.com
Sara Tucker, Brooke Walters, Jeff Applegate, Carl Weimer
With special thanks to the Ball Aerospace OAWL development team & partners, including Mike Hardesty and Sunil Baidar of CU-CIRES/NOAA

## Slide 2: Optical Autocovariance Wind Lidar (OAWL): Field-Widened, Dual-Wavelength-demonstrated, Quadrature Mach Zehnder Interferometer (QMZI)
A
A
O

0

/2
/4
QWP = π/2
3π/2
0 (2π)
PBS
π/2
π
PBS
Non-Polarizing beamsplitter
Field-widened using all-reflective cat-eye design
Quarter wave plate (QWP) + polarizing beam splitters (PBS) provide four relative phase interference points.
OPD = optical path difference
Demonstrated OAWL SYSTEMS Year & Name | Wavelength(s)* |  | Aerosol | Molecular | Ground | HSRL | Airborne | #Looks
 | 355 nm | 532 nm |  |  |  |  |  | 
2011, OAWL-P IIP | X |  | X |  | X | X | X | 1
2013, HOAWL | X | X | X |  | X | X |  | 1
2016, GrOAWL |  | X | X |  | X | X | X | 2
2017, HAWC-OAWL | X | X | X |  | X | X | O | 2
2018, StratOAWL | X |  | X | X |  |  | X | 1#
2020+, Nested OAWL | X | X | X | X | X | X |  | 2
*Reflective cat-eye approach provides wavelength flexibility. 1064 nm concept also considered for high aerosol applications. # Balloon-based on scanning gondola |  |  |  |  |  |  |  | 
Interferometer field-widening enables use of larger system field of view (like CALIPSO), reduces telescope requirements, and enables modularity

## Slide 3
Green OAWL (“GrOAWL”)
Airborne demonstrator for 532 nm Aerosol winds: (flown on WB-57)
Dual 45 Line-of-Sight (LoS) wind speed data – can combine to get speed & direction
Tucker et al., 2018 & Baidar et al., 2018, J. Atmos. & Ocean. Tech,
Variable wind speed processing parameters: 0.5-20 s accumulation, 8.5 m to 1 km range gates based on aerosol loading
HAWC-OAWL
Dual wavelength (355 nm & 532 nm) OAWL aerosol winds (could build for 1064 nm too…)
Concurrent dual wavelength HSRL (no crosstalk) for aerosol backscatter coefficients
Ground-based observations Pointing 30 El, ~270 Az.
Backscatter - km-1sr-1
OAWL 532 nm aerosol backscatter coefficient
17 June 2016: Forward look, 1s profiles, <1.5 mJ/pulse (0.3 W), 532 nm
Aft look, 1s profiles
LOS Wind Speed, m/s
LOS Wind Speed, m/s
Airborne OAWL Configurations & Demonstrations Ground-Based

## Slide 4: ATHENA-OAWL Earth Venture Instrument (EVI) proposal for ISS
ATHENA-OAWL: Aerosol Transport, Hurricanes, and Extra-tropical Numerical weAther using OAWL.
Path-finding science for next-generation global weather prediction and climate analysis: co-located wind and aerosol (HSRL) profiles to address multiple dynamics and aerosol science questions
Design-to-cost approach to NASA EVI based on heritage systems (i.e., CALIPSO) & International Space Station
Proposed in 2013 (Cat 3) and Re-proposed in 2016. Rated Category 2 in 2018 (Selectable), not selected  Aeolus launched August 2018.
Designed for Japanese Experimental Module: JEM-EF
  Provides large margins on mass, power, cooling availability
  Limited slot availability
ISS not an option for Earth Venture proposals since 2018
RAM direction
ISS Ground
Track
Notes: Objectives: Co-located wind and aerosol profiles to provide:
  better understanding of relationships between aerosol radiative forcing, atmospheric dynamics and the genesis and lifecycle of tropical cyclones
  understanding of the impacts of long-range dust and aerosol transport on global energy and water cycles, air quality, and climate.
  breakthroughs in modeling and prediction of low and mid-latitude weather and climate.

## Slide 5: Internal Free-Flyer study in support of Next Generation Weather Architecture
Free-flyer OAWL studies to support future NOAA LEO portfolio and NASA Earth Explorer concepts
Objective – provide a valuable wind observation in a low-cost mission concept
Approach: take advantage of the following:
  Growth in launch and spacecraft technology markets
  OAWL design modularity and optical throughput efficiency
  High TRL components from the CALIPSO lidar, etc.
Focused on a smallsat solution to optimize performance and cost
Notional instrument concept chosen based on ATHENA-OAWL design for ISS – with option for 355 nm.
Single line of sight (LOS), ESPA-Grande-compatible concept (for potential rideshare)
  2016: Demonstrated the dual LoS OAWL system in remote aircraft testing – 2 looks still an option for future missions.
  Two spacecraft, each with single LoS, provide more information than 1 spacecraft with dual LoS. - like the “Dual Tandem” approach discussed by Stoffelen
  Also see Horanyi et al., and presentations at Aeolus CalVal meeting.

## Slide 6: Free Flyer OAWL – Internal Study
Baselined a “sensorcraft” approach, starting with Ball small spacecraft (e.g. STPSat) components, avionics, etc. in an “ESPA-Grande” volume
  Fit a single-look (single laser line of sight) system - like Aeolus, but smaller.
  Concept maximizes science return given requirements and constraints
  Supports 300 – 500 km altitude
  Minimum 5 years consumable life for spacecraft resources.
Considered wide range of mission factors:
  Orbit – power/eclipses, battery sizing, cooling capability, required fuel, etc.
  Spacecraft volume/compatibility, pointing, drag, etc.
Optimized power-aperture product based on spacecraft volume, desired sun-sync orbit, and laser TRL
Bus and payload packaged around an 85 cm diameter telescope & 500W wallplug laser (with required cooling in desired orbit) – and room for small IR sounder
Looking into rideshare vs. dedicated launch options to enable mission within budget concepts
Increasingly lower launch and spacecraft costs enable a wind lidar + sounder concept for a future Earth Explorer mission.
This design is compatible with the various flexible OAWL configurations…
  Radiometric performance results available for various orbits & power levels for each modular configuration.

## Slide 7: OAWL Developments: a molecular channel for UTLS winds
Why? Coverage (esp. in UTLS)
Aeolus impact, previous OSSE’s
OAWL/QMZI approach has been demonstrated for aerosol winds
We can also use QMZI make wind measurements from molecular returns
  with or without knowledge of aerosol returns
  No aerosol contamination of molecular (Rayleigh) channel
Aeolus Molecular (Rayleigh)
Aeolus Aerosol (“Mie”)
Aeolus data images: ESA & ECMWF
A
A
A
Lidar returns increase at cloud layers, with reduced returns after the cloud returns
Heterodyne Detection
A
~2 μm, (1.6 μm, ~10 μm)
“Direct” Detection
Double-Edge
Fringe Imaging
Mach Zehnder
M
1064 nm, 532 nm (CALIPSO) & 355 nm (Aeolus)
A
From http://www.swa.com/ target-atmosphere-profiles
These properties factor strongly into which lidars are best for a given application

## Slide 8: Path(s) to Full Atmospheric Wind Profiles
Aeolus - all 355 nm wavelength
    Molecular (Rayleigh): Double-edge Fabry-Perot etalon
    Aerosol/Cloud (Mie): Fizeau etalon spectrometer
OAWL field-widened QMZIs
  Two 355-nm wavelength QMZIs
    Molecular: Compact, short (~3-4 cm) OPD QMZI -
      StratOAWL - on stratospheric balloon under a DARPA program
    Aerosol: Long (90 cm) OPD QMZI (original OAWL configuration)
      Demonstrated under NASA IIPs (dual wavelength aerosol winds)
      Alternative: Fizeau spectrometer like on Aeolus
  355 nm & 532 nm: The Nested-OAWL interferometer
    Aerosol winds @ 532 nm (long OPD – like previous OAWLs)
    Molecular & aerosol winds @ 355 nm (new short OPD)
    Same laser used on HAWC-OAWL and GrOAWL
    Interferometer & laser frequency stabilization not required
    Internal breadboard build & demonstrations: 2019-2020
Short-OPD, 355-nm QMZI OAWL
Long-OPD, 355-nm QMZI OAWL – or Fizeau
Nested short (355 nm) and long (532 nm) OPD QMZIs
Notes:     Short (molecular) OPD is “nested” inside the long (aerosol) OPD: “Nested OAWLs”
    Same detectors as used for the dual wavelength OAWL
    2018 IRAD for demonstration is underway

## Slide 9: Nested-OAWL demonstration: 05 January 2020
Ground based operation in Boulder (1.6 km altitude)
LOS: ~275 azimuth, ~30 elevation using a turning mirror below the system
Maximum sampling range of ~34 km (~19 km altitude @ 30  elevation )
355 nm (top panel)
  Short (0.04m) OPD molecular + aerosol channel
  large FSR  no wrapping but higher uncertainty
  ~11 mJ/pulse, 200 Hz, (effective ~4.5 mJ/pulse from turning mirror R=0.652 @ 355)
532 nm (bottom panel)
  Long (0.9m) OPD aerosol (“Mie”) channel
  Small FSR - lower uncertainty
    if/when aerosols are present
    Proven 532 nm channel provides validation for 355 nm molecular channel
  ~1 mJ/pulse, 200 Hz.
  Wind estimates outside the FSR wrap 2, but can typically be unwrapped  they are not lost (like in heterodyne & filter-based approaches)
Preliminary data – algorithm development (incl. ML) in progress
Speed (m/s)
Speed (m/s)
Molecular + Aerosol winds
Aerosol only winds

## Slide 10: Nested-OAWL: 21 October 2020 (smoke layer)
Molecular + Aerosol winds
Aerosol only winds
1s, 26m
5s, 64m
355 extinction dominates by ~12 km AGL  A downward-looking (airborne, space-based) system would balance extinction with increasing molecular backscatter vs. range

## Slide 11
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ‘30
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ‘29 | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ‘28 |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ‘27 |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ‘26 |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ’25 |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ‘24 |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  | ‘23 |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | ‘22 |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | ‘21 |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | ‘20 |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ‘19 |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | ‘18 |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | ‘17 |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | ‘16 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  | ‘15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | ‘14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ’13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | ‘12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | ’11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | ’10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
’09 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Ball Aerospace’s Optical Autocovariance Wind Lidar (OAWL) - Aerosol & Molecular
Nested OAWL full troposphere
demonstration
OA Laboratory Prototype
OAWL Mission concepts
EVI-4 ATHENA-OAWL 532 nm Aerosol winds ISS Mission concept (TMCO rated Selectable)
Operational Airborne mission development
Operational Space Demonstration Flight build
Full tropospheric operational wind lidar
On-orbit Operational Demonstration
GOING BEYOND: NASA/Ball CALIPSO Lidar >14 Years on orbit!
ESA’s ADM Aeolus (single look – 355 nm Aerosol & Molecular)
Global 3D winds
ESA’s Aeolus Launch
22/08/18
NSOSA study
ESDS
*OAWL-IIP 2011 demo
*OAWL-ACTs
*GrOAWL 2016 demo
*NASA ESTO funded grants (no profit)
Ball funded (IRAD, studies, etc.)
aerosols
winds
*HAWC-OAWL IIP
Aeolus CalVal studies
Free Flyer OAWL: ESPA-class wind lidar Mission Concept Study
OAWL provides the highest US TRL for a Doppler Wind Lidar mission
Notes: OAWL IIP – First demonstration 2011
GrOAWL: the 2 LOS ATHENA Airborne Demonstrator built, flown, validated, and scaled to space
  2 pubs: Journal of Atmospheric & Oceanic Technology: Tucker et al., 2018 & Baidar et al., 2018
ATHENA-OAWL: EVI-2,4 proposals
  Aerosol Transport, Hurricanes, and Extra-tropical Numerical weAther using OAWL.
  Mission Systems Architecture: Design-to-cost approach: based on heritage systems (CALIPSO) and ISS hosting
  EVI-4, rated Category 2 (TMCO rated Selectable – but not selected).
HAWC-OAWL: Ground-based demonstrations of dual-wavelength wind and aerosol backscatter coefficient measurements
ESTO managed competitive grants: NO profit

## Slide 12: Summary & Conclusions
ESA-Aeolus’ successes and lessons benefit the whole community
  Lidars can provide direct winds measurements from space; the technology is available.
  Aeolus is demonstrating the impact of full tropospheric wind measurements
And yet, we (the whole community) can do more, right away – starting with ongoing Aeolus tests, then Aeolus follow-on, then US missions
The OAWL QMZI technology provides a demonstrated, high TRL, low risk approach to a US aerosol wind lidar mission
A 3D-winds mission can also include sounders, and lidar will provide innovation
OAWL QMZI technical benefits include:
  High throughput/optical efficiency to optimize mission size, weight, and power
  Flexibility to provide Winds + HSRL at various wavelengths (1064, 532, 355)
  Demonstrated options for including a 355 nm molecular channel (like Aeolus) for UTLS observations
Ball continues to invest in OAWL to provide wind observations through the full troposphere and to be a mission partner, supporting future 3D winds missions.
Thank you for listening
Notes: Since 2017, NASA is only investing in coherent (2 micron) lidar systems. 2 micron system TRLs are low and still require significant development.
No NASA investment in molecular wind lidar systems since 2014

## Slide 13
OAWL: Full tropospheric wind & aerosol observations
NASA/Ball CALIPSO Aerosol Lidar
2006
ESA’s Aeolus Wind Lidar
2018

## Slide 14: EXTRA, EXTRA!

## Slide 15: OAWL builds on Aeolus & CALIPSO – and relaxes technical requirements
Field widened interferometer (~10 mrad+) mitigates biases from changing field angles, provides Tx/Rx overlap margin, and enables use of lower cost (not diffraction limited) telescopes
OAWL QMZI configurations for aerosol & molecular channels: no cross calibration required & no Mie contamination
OAWL detectors & real-time processors increase flexibility in processing parameters, altitude gate size, etc.
Wrapping fringes for removal of platform-motion-induced Doppler offsets or high speed winds in processing without signal loss
OAWL QMZI high throughput efficiency optimizes lidar power-aperture design
Wrapping fringes eliminate need to lock QMZI to laser frequency
Laser - Nd:YAG: doubled (like CALIPSO) and/or tripled (like AEOLUS)
Like Aeolus, OAWL offers a path to full atmospheric lidar wind profiles

## Slide 16: Observing Atmospheric Winds from Space
Optical (feature tracking lidar)
Optical Doppler Lidar
A
M
Molecular: UT/LS
Aerosol: LT/clouds
Measure 3D Winds
Active
Passive (Motion Vector, sea-state, etc.) Sounders and Imagers
Microwave
IR
W
Water Vapor Features
W
A
Lower troposphere/ aerosol scattering
A
Full-Troposphere & Lower Stratosphere (aerosol + molecular)
M
A
“Coherent” Heterodyne Detection
A
LaRC
DAWN
~2 μm, (1.6 μm, ~10 μm)
NOAA CSD, NOAA P-3, Halo, Leosphere,
“Direct” Detection
Double-Edge
Fringe Imaging
Mach Zehnder
A
M
A
M
A
M
ESA’s Aeolus
GSFC?
UPMC (France)
ATHENA OAWL
1064 nm, 532 nm (CALIPSO) & 355 nm
Nested OAWL
-wave
MWIR
visible
Notes: Plenty of solutions – the challenge is asking the right questions
~40 years of NASA investments in wind lidar technology
  Multiple technology investments from NASA ESTO.
NASA/NOAA Working Group on Space-Based Wind Lidar (“LWG”, formerly the LAWS science team, 1989)

## Slide 17
Courtesy - Ivan Clark, NASA

## Slide 18: Mission motives – really-simplified
Global initialization of forecast models that use tested model physics
  Global coverage
  Variable scales (model grids)
Research on model physics
Research to update model physics
  Focused coverage
  Variable scales
  PBL emphasis
  ESDS driven science
A well-planned mission can provide something for everyone
NOAA Requirements: focus on improving NWP, Protecting Lives and Property
NASA Requirements: Science. Processes, Modeling, Pre-operational

## Slide 19: To think about: Shaping a future US wind lidar mission starts now
What does NOAA and, specifically, NESDIS & the NWP community hope to get out of a winds mission?
  Full troposphere vs. certain parts?
  Large scale global winds from orbit?
  Detailed PBL studies (from aircraft/surface obs)?
What is the maximum resolution (horizontal-along track, and vertical) that supports an operational demonstration?
  Is Aeolus resolution & performance good enough?
  What data/science improvements are desired over Aeolus?
  What are we willing to trade to keep costs down? Resolution? Duty cycle? Vertical coverage? Horizontal coverage?
How many look-angles or lines-of-sight?
  Aeolus finding (Horanyi et al. 2014): Single LOS provides 60%-70% the impact of dual-LOS on same satellite.
  Assimilation: LOS winds provides more impact than horizontal winds
  Two looks on same satellite, or two smaller satellites for double coverage?
How would you take advantage of variable/flexible sampling/processing?

## Slide 20
History: A partial (38 year) timeline of space-based Doppler wind lidar
CO2
Solid State Heterodyne
GTWS
GWOS
WISSCR
ATHENA-OAWL
DAWN 1 IIP
DAWN 2 IIP
CCOPE/ADLS (Airborne)
NOAA TeaCO
NOAA Mini-MOPA
LAWS Panel
LAWS Team
SPARCLE
NOAA HRDL
VALIDAR
 DAWN Flights 
ESA’s ADM Aeolus (single look – 355 nm Aerosol & Molecular)
Decadal Survey 3D-Winds Hybrid
Aeolus Launch
Direct Detection
Edge Technique
Fringe Imaging HRDI
Zephyr
GLOW Double Edge
Fringe Imaging Lidar
GroundWinds
A2D Airborne
Optical Autocovariance
TWiLiTE IIP
TWiLiTE AITT
 TWiLiTE Flights.
Optical Autocovariance (OA) Wind Lidar
84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 00 | 01 | 02 | 03 | 04 | 05 | 06 | 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22
DAWN SP
Notes: ~40 years of NASA investments in wind lidar technology
  Multiple technology investments from NASA ESTO.
NASA/NOAA Working Group on Space-Based Wind Lidar (“LWG”, formerly the LAWS science team, 1989)
2007 NRC Decadal Survey “3D-Winds” mission (Tier 3): defined as a hybrid of two separate lidar systems, with two different lasers, on one spacecraft.
The past decade:
  Risk tolerance at NASA has decreased significantly
  Budgets have decreased as well: NASA asked to do more and more
  Industry technology investments help to make missions possible
  Contractor efforts are increasingly scrutinized/audited (DCAA)

## Slide 21
Based on NOAA’s Satellite Observing System Architecture (NSOSA) Study
Next Generation Operational LEO Weather Architecture