## Slide 1: Aeolus, ESA’s wind mission Status and future outlook Tommaso Parrinello on behalf of the Aeolus Team
NOAA-NASA Working Group
on Space-based Lidar Winds
17-19 November 2020

## Slide 2
A successful Track-Record
ESA-Developed Earth Observation Missions
ESA UNCLASSIFIED – For Official Use
European Space Agency
Notes: D/EOP has three main lines of activities: Earth Science, Copernicus and Meteorology
Since the latest launch of Aeolus on 22 Aug. 2017, we have 25 satellites in development and 15 satellites in operation.

## Slide 3
Launched: 22 August 2018, Kourou
Launcher: Vega
Main Payload: ALADIN - DWL @355 nm
Orbit: Altitude of 320 km, inclination of 97, sun-synchronous, Dawn-Dusk, 7d repeat cycle
Mission Control: ESA/ESOC (DE)
Ground Station: Kiruna (SWE), Svalbard (NOR) and Troll (Antarctica)
Data Processing: Tromsø, (NOR), ECMWF (Reading, UK), ESA/ESRIN (IT)
Mission Management: ESA/ESRIN (ITA)
Mission Life: 3 years
Aeolus, European Space Agency’s Wind Mission

## Slide 4: AEOLUS MISSION OBJECTIVES
Scientific Objectives
To improve the quality of weather forecasts by providing global measurements of horizontal wind profiles in the troposphere and lower stratosphere
To advance our understanding of atmospheric dynamics and climate processes
Long-term goal
Demonstrate space-based Doppler Wind LIDARs capability for operational use

## Slide 5
Example of Direct wind observations in the GOS: radiosondes, surface (conventional, scatterometers), airplanes, AMVs
Motivation
Wind observations are scarce in the present Global Observation Systems which limit our ability to predict weather especially in the tropics where atmospheric motions on all scales are dominated by the wind field …. …and expect to obtain information on aerosol and cloud properties
(Aeolus Science Report)
Aeolus, European Space Agency’s Wind Mission
Notes: Motivation: lack of winds in the GOS
Direct wind observations in the GOS:
radiosondes, surface (conventional, scatterometers), aireps, AMVs
Aeolus observations per day:
~0.2% of the 40 million
but significant forecast improvement still expected and seen

## Slide 6: MEASUREMENT PRINCIPLE
The line-of-sight (LOS) points 35o from nadir to capture profiles of single component horizontal wind (LOS wind is projected to HLOS)
Direct detection UV Doppler Wind Lidar (355 nm) on two receiver channels: Rayleigh to determine winds from molecular backscatter and Mie to determine winds from aerosol & cloud backscatter
Weekly calibration to monitor instrument drifts and ground returns for attitude correction are used for instrument calibration (bias correction).
Vertical wind resolution: 24 vertical bins per channel, 250m-2km
Horizontal wind resolution: 87 km for Rayleigh, 10 km for Mie
Notes: Direct detection UV Doppler Wind Lidar (355 nm) on Two receiver channels: Mie receiver to determine winds from aerosol & cloud backscatter (Fizeau) & Rayleigh receiver to determine winds from molecular backscatter (Double edge Fabry-Perrot)
Horizontal resolution: Horizontal wind resolution (87 km for Rayleigh, 10 km for Mie). Can be optimised. L2A is currenrly given at 87 km
24 vertical bins per channel (old technology, much better resolution can be achieved now!)
Vertical sampling: 250m – 2 km, steps of 250m
Sampling optimized to climate zone (max 8 times per orbit)

## Slide 7: ALADIN: A TECHNOLOGICAL CHALLANGE
One of the most sophisticated instruments ever to be put in orbit
High-power ultraviolet (UV) laser transmitter containing ~80 optical functions and different wavelength conversion
Extreme backscatter sensitivity via 1.5m telescope, 80 microns field stop and etalon spectrometers
Doppler Wind Lidar principle
  𝚫f = 2*fo*VLOS/C
  VLOS=1 m/s
    𝚫f = 5.64 MHz - 𝚫f /fo = 6.7 10-9
    𝚫λ= 2.4 10-15 m (H+ ≈ 1.7 10-15 m)

## Slide 8: SPACE SEGMENT
It is performing well and any sign of degradation, including consumables and life limiting elements, are within the specifications. Special operations tasks exceed any explorer missions
FM-B continues to perform well in terms of UV output energy (i.e. around 61mJ) and stable since March 2020.
The most critical problem remains the decrease of the return signal. Very close to FM-A swap but less impact on data quality
Investigations with ESA, industry and external expert teams are taking place incessantly. An overall roadmap to recapture the energy has has been defined and it constantly and dynamically amended
The fully recovery is probably not realistic but different solutions and mitigations actions are taking place (e.g. M1 thermal optimisation) including also options like returning to FM-A and/or to lower the orbit.
The performance of the mission is very good
Output UV Energy
INT Signal
ATM Signal
Courtesy O. Lux (DISC)
Mission extended to end of 2022
Notes: MENTION the sensitivity of the return energy to thermal environment in particular to the eclipse season
LID---> Laser Induced Damage (in the optics)
LIC- Laser Induced Contamination (in the optics)
The option to return to FM-A is based on the idea that the laser beam drift might be linked to the FM-B transmitter (rigid body motion) or loss of alignment. This behavior was not present in FM-A where the decrease of energy followed exactly the same loss of output energy.

## Slide 9: GROUND SEGMENT
Constantly monitoring, improving and managing the Aeolus data acquisition, production, reprocessing and distribution to user community (e.g. ~98.0% L2B products are available to users in NRT)
Weekly ALADIN instrument Mission Planning operating in accordance to mission objectives, wind observation requirements, instrument maintenance and calibration activities like the recent IRONIC
VirES for Aeolus (interactive data visualization and retrieval platform) https://aeolus.services/ now allows self-registration for public users. Roadmap for future evolution into a Virtual Collaborative Environment is under implementation
Svalbard Station

## Slide 10
Constant monitoring and improving of Aeolus data quality (random and systematic errors) allowing for quick reaction to performance issues.
    Random errors are not improving because primarily affected by reduced return atmospheric signal and lower UV emitted energy. Biases have improved significantly
    Adopting rapid six-month major update cycles of ground processors, allowing swift adaption to lessons learnt and operational/scientific needs, has been successful.
    The reprocessing strategy is quite stable but always open to feedback
New evolution are taking into consideration the outcome of the ongoing investigations, reprocessing strategy and synergies with other Mission (e.g. ATLID EarthCARE algorithms for L2A Aeolus products)
Mission Requirements
April - June 2020
QUALITY AND DATA EVOLUTION

## Slide 11: SCIENCE
ECMWF, DWD and Météo-France assimilating Aeolus data. UK MetOffice by end of 2020. NCMRW by Feb. 2021
Impact of Aeolus on NWP and on other scientific exploitation (i.e. aerosol, gravity waves, hurricane tracking, atmosphere dynamics) confirmed at the recent Aeolus Cal/val & Science Workshop
Aeolus+ Innovation studies under negotiation
Aeolus scientific study (i.e. prediction on extreme weather events and regional model) under preparation
Aeolus optical products L2A are becoming more mature and ready to be released in spring 2021
Standard deviation of change in zonal wind analysis (m/s) at ~10 km in the ECMWF model when assimilating Aeolus Rayleigh – clear + Mie-cloudy winds from 4 April to 19 August 2020, courtesy M. Rennie ECMWF
Notes: Indian National Centre for Medium Range Weather Forecasting (NCMRW) will by February 2021

## Slide 12
WindVal III (Central Europe, Nov 2018) Successfully completed
AVATARE (Central Europe, May 2019) Successfully completed
AVATARI (Iceland Arctic, September 2019) Successfully completed
STRATEOLE2 (Seychelles, Nov. 2019 - Feb. 2020) Successfully completed
TROPICAL (Cape Verde/Tropics, Summer 2020) Re-planned to Summer 2021 due to Covid-19
Aeolus Airborne Campaigns (2018-2021)
AEOLUS AIRBORNE CAMPAIGNS (2018-2021)

## Slide 13
Mission Timeline (2020-2022+)
Release L2A
Spring 2021
End nominal life-time
December 2021
2020
PB-EO Decision
Mission Extension
September 2020
2021
FM-B Reprocessed #1
Fall 2020
Signal Recovery
Fall-Winter 20/21
GO-NO for
Next steps (OL, FM-A, etc)
Spring 2021
PB-EO ME
Spring 2022
2022
Aeolus re-enters
2.0 ANX
Spring 2021
OL (or FM-A)
TBC
Orbit decay/FM-A on
Major Baseline
Spring 2021
FM-B Reprocessed #2
Spring 2021
Tropical Campaign
Summer 2021
Major Baseline
Fall 2021
FM-A Reprocessed #1
Fall 2021
Major Baseline
Spring 2022
Full Reprocessed
Fall 2022
Major Baseline
Fall 2022
OL (or FM-A )
TBC
Orbit decay/FM-A on
End Extension
December 2022
EGU 2021
Science & CV Workshop
SAG#3
NWP/L2A WS
SAG #2
SAG#4
CaV& Science Workshop
SAG#5
EGU 2022
Science & CV Workshop
SAG#6
NWP/L2A WS
SAG #2
Mission Extension Beyond 2022

## Slide 14: SYNOPSIS
    The overall performance of the mission is good. After the switch to FM-B, a number of critical issues remain challenging with the instrument and will drive the timeline and operations in the following months.
    Aeolus has been providing global measurements of horizontal wind profiles for more than 25 months (>3B shots). Main bias variations have been corrected. Improvement of Random Error to meet Mission Requirement remains challenging
    The recent workshop has confirmed the impact of Aeolus L2B winds is consistent in several global models with largest effects in the upper troposphere and lower stratosphere, in the TR and SH. Further scientific exploitation of the data is showing significant results
    Several met centers are assimilating (or about to assimilate) Aeolus data into their operational forecasting systems.
    The mission has been extended until end of 2022. Our main objective is to reach that target with the best possible performance and in support of the follow-on development