## Slide 1: The role of ADWLs in the design, performance simulations, trade studies and cal/val of space-based wind observing systems
G. D. Emmitt, S. Greco and S. A. Wood
Simpson Weather Associates
M. J. Kavaya and K. M. Bedka
NASA/LaRC
NOAA-NASA Working Group on Space-based Lidar Winds
Virtual meeting
17-19 November, 2020

## Slide 2: ADWLs available for wind observations, especially over oceans
TODWL (ONR, Naval Postgraduate School)
P3DWL (Army Research Laboratory/NOAA )
DAWN (NASA, LaRC)
DLR A2D and 2um coherent system (DLR)
Near future
  AWP (NASA/LaRC)
  OAWL (Ball Aerospace)

## Slide 3
DAWN
P3DWL
DLR DWLs

## Slide 4: Papers relevant to this presentation (last 3 years) (TODWL, P3DWL and DAWN)
Bucci, L., S. Majumdar, R. Atlas, B. Dahl, G.D. Emmitt and S.A. Wood, 2020: Impacts of Assimilating Airborne Doppler Wind Lidar data into NOAA’s Hurricane Weather Research and Forecasting (HWRF) System. 34th Conference on Hurricanes and Tropical Meteorology, New Orleans, LA, May. 12
Cui, Z., Z. Pu, G.D. Emmitt and S. Greco, 2020: The Impact of Airborne Doppler Aerosol WiNd lidar (DAWN) Wind Profiles on Numerical Simulations of Tropical Convective Systems during the NASA Convective Processes Experiment (CPEX). Journal of Atmospheric and Oceanic Technology, Accepted for publication, February 28, 2020.
Emmitt, G.D. and S. Greco, 2020: Using an Airborne Doppler Wind Lidar to Evaluate Sampling and Data Processing Strategies Relevant to PBL Research and a Future Space-based System. Amer. Meteor. Soc. 100th Ann. Meeting, , 10th Symposium on Lidar Atmospheric Applications Poster Session, Boston, MA, Jan. 13.
Greco, S., G.D. Emmitt, S. Wood, K. Bedka and S. Rodier, 2020: Comparison of DAWN, Dropsonde and Aeolus Wind Observations during the April 2019 NASA Aeolus Cal/Val Test Flight Campaign. Amer. Meteor. Soc. 100th Ann. Meeting, 16th Annual Symposium on New Generation Operational Environmental Satellite Systems, Boston, MA, Jan. 16.
Greco, S., G.D. Emmitt, S. Wood and M. Kavaya, 2019: Potential ABL wind measurements and derived parameters from a space-based coherent Doppler Wind Lidar. AGU 100th Fall Meeting, A11T – Observing the Boundary Layer from Space II Poster Session, San Francisco, CA, Dec. 9.periments (OSSEs)—Part II, Phoenix Az., January 8
Emmitt, G. D., M. Kavaya and U. Singh, 2017: Integrating a Doppler wind lidar into a network of wind observing systems: Capitalizing on synergisms with a high precision, cloud scene penetrating lidar. 2017 IEEE International Geoscience and Remote Sensing Symposium (IGARSS), Fort Worth, TX, USA,23-28 July 2017.

## Slide 5: Papers/presentations relevant to this presentation (most co-authored with NASA and NOAA researchers)
Decade | OSSEs | Data Assimilation | Instrument design/trade studies | Cal/Val
2011-2020 | 21 | 15 | 10 | 9
2001-2010 | 52 | 8 | 21 | 5
1991-1999 | 17 |  | 16 | 
Source: http://www.swa.com/research-library/eld-library

## Slide 6: Space-based wind observing system (s): mission phases
Requirements
Concept construction (OSSEs)
  DWL instrument error (random and bias) can be traced to ADWL observations
Detailed design and trade studies (OSSEs)
  Airborne demonstrations of the technology
DWL data processing and product generation
  Developed with airborne DWL data
Post launch cal/val
  ADWLs able to cover significant expanses of ocean
Post launch product improvement
  ADWLs plus companion sensors (e.g. HALO, dropsondes) can provide oversampling with precise wind and aerosol measurements

## Slide 7: Requirements for space-based wind observations
Science/application justification
  Global weather forecasting
  Global PBL research
  Global full tropospheric/stratospheric research
Precision
Coverage
  Temporal
  Spatial
Latency
Data management

## Slide 8: Space-based DWL concept development
Instrument feasibility/trade studies (built upon ADWL experience)
  Single/hybrid technology
    Aeolus approach; Direct Mie and Rayleigh
    Coherent Mie; Direct Rayleigh
  Synergistic technologies
    Active lidar and passive AMVs
  Multi parameter missions
    DIAL plus DWL

## Slide 9: ADWL support for simulations for OSSEs
Coherent or Direct
Passive AMVs
Emphasis in simulating optical remote sensing of winds for OSSEs has been clouds and turbulence/shear.
Characterization of instrument measurement errors based upon ADWL downward looking perspective (clouds, aerosols, surface reflections)
  Random errors
  Bias (more important)
Sampling errors derived from sub-sampling high quality/high density ADWL observations.
  Representativeness
  Situational bias (e.g. clouds permitting)

## Slide 10: Other space-based DWL simulations
LAWS (EOS proposal); 1989-1993
GTWS (NPOESS and data buy); 1996 -1998
SPARCLE (NASA Shuttle); 1997-2001
DD/Hybrid (Gentry at GSFC); 1999-2001
Tech neutral DWL OSSEs (NCEP); 2000-2003
JEMCDL (Japan); 2001-2003
GeoWinds (NASA); 2001
ALADIN (ESA); 2008
GWOS (NOPESS); 2008-2012
WISSCR (a Coherent DWL for ISS); 2011-2012
OAWL (free flyer); 2011-2015
OAWL (ISS); 2014-2015
WINDSP (under development); 2017 - present

## Slide 11
MODTRAN PBL VALUES
Some data bases support
1-2 orders of magnitude
higher backscatter in the
near surface than
we have been using in
our simulations.
These beta profiles are
based upon data
collected during
NASA and European
airborne campaigns
in addition to verification
by ground based lidars
with coherent detection
http://www.swa.com/images/LidarSpaceBased/Design%20atmospheres%20for%20GTWS.pdf

## Slide 12: Simulated potential WIND-SP vertical coverage
NO CLOUD
BACKGROUND
AEROSOLS
(e.g. SH, ARCTIC)
W/CLOUDS
ENHANCED
AEROSOLS
(e.g. Anthro, deserts,
fires, thin clouds
Remember the 90/10 rule

## Slide 13: Data processing and product generation practice using ADWL data before launch
Adaptive Integration Algorithm (AIA)
Supervised Search Algorithm (SSA)
Multi-pass Micro Slides (MMS)
Multiscale Turbulence Metric (MTM)
Sea Spray and Foam Detection Algorithm (SSFDA)
Wave State Metric (WSM)

## Slide 14: Identifying MABL properties observable from space using ADWL based algorithms
Profiles of the horizontal wind vector using two perspectives
  Maximum vertical resolution ~ 33m in high backscatter situations
  Nominal horizontal resolution ~500m in high backscatter situations
Depth of the MABL defined by backscatter gradients
  Vertical resolution using sliding gates ~ 10-25m for well defined ABL tops
Depth of the mixed layer using the spectral width
  Limited to cases where TKE > 1.0 m^2/s^2 near top of PBL
Shear within the MABL
  Presence of LLJs which have a significant impact on estimating air/sea exchanges
Presence of rolls within the MABL
  Allows for selection of appropriate parametrization of the ABL fluxes
Depth of sea spray layer and presence of foam
  Large impact on air/sea fluxes; spray enhances fluxes while foam reduces fluxes
Additional observations of surface currents and waves in high impact situations

## Slide 15: ADWL data Processing Package for the mABL (AP3BL)
PBL heights derived from aerosols and turbulence
PBL turbulence intensities used with other space-based observables to estimate fluxes
Detection of the presence of LLJs and OLEs within the MABL
Sea State (waves, foam, currents)
LAS (Layer Adjacent to the Surface) aerosol gradients and structures

## Slide 16: Detailed design stage for DWL instrument
ADWL data and experience are critical to optimizing instrument design to verifiable performance expectations
  Sampling patterns and integrated shot density
  Observation precision vs coverage
  Vertical resolution vs. PODs
  Derived quantities based upon ADWL experience
    Cloud top/bottom
    PBL depth
    Aerosols
    Turbulence
    Ocean surface properties (waves, foam, currents)

## Slide 17: Using airborne DAWN to simulate space-based DWL sampling and representativeness
For example, WIND-SP design evolves from the DAWN instrument
Data quality expectations are based upon proven DAWN performance
Ongoing analyses of DAWN data taken during CPEX (2017) and the AEOLUS cal/val preparatory flights (2019) has a WIND-SP focus
DAWN’s optical power allows for single shot processing from 10 km and thus provides an excellent high spatial representation of the winds over planned WIND-SP 10km flight segments.
Using only 2 of the 5 looks by DAWN during the CPEX allows for evaluation of the 2 looks (or single look) data products WIND-SP.

## Slide 18: DAWN wind profile from Flight Level 10km using 2 second stares and 32m range gates

## Slide 19: Example of a 200HZ space-based DWL sample density overlaid on ~ 100km of DAWN single shot data during Aeolus cal/val
~100 km
10 km
Cloud

## Slide 20: DAWN 100 km stare along Aeolus observation plane: VLOS (m/s)

## Slide 21: Post launch cal/val & post launch product improvements

## Slide 22: DAWN, Dropsonde and Aeolus Wind Comparisons from April 2019 NASA Aeolus Cal/Val Test Flight Campaign
Aeolus Cal/Val and Science Workshop
2-6 November 2020
G. D. Emmitt and S. Greco
Simpson Weather Associates
M. Kavaya and K. Bedka
NASA/LaRC
NASA Airborne DAWN and HALO underflights of Aeolus
April 17-30, 2019 based out of Palmdale, CA
Airborne DAWN, HALO and YES Dropsondes aboard NASA DC-8
5 underpasses of Aeolus
Over the eastern Pacific Ocean
- Two transects between US west coast and Hawaii
- Three missions off west coast of US (30 – 50 N)
- Mostly clear to partly cloudy conditions
- Low and high aerosol segments
DAWN profiles every ~5km ; 128 DAWN profiles along 600km track
7 AEOLUS profiles along DAWN under-flight track
7 DAWN “Integrated” profiles utilizing 17 individual DAWN profiles

## Slide 23: Coherent DWL DAWN prepping for Aeolus underflights planned for summer 2021
Date | # of U Samples | Mean ∆z (m) | Bias (m/s) | RMSD (m/s)
ALL | 4327 | 3.06 | -.13 | 1.01
0422-23 | 1453 | 3.33 | .04 | 0.88
0425-26 | 476 | 2.65 | -.01 | 1.00
0427-28 | 702 | 2.93 | -.61 | 1.19
0429-30 | 1697 | 3.00 | -.11 | 0.97
DAWN- dropsonde comparisons during April 2019 Aeolus underflights
Date | # of V Samples | Mean ∆z (m) | Bias (m/s) | RMSD (m/s)
All | 4327 | 3.06 | -.18 | 0.90
0422-23 | 1452 | 3.33 | -.20 | .78
0425-26 | 476 | 2.65 | -.53 | 1.01
0427-28 | 702 | 2.93 | .01 | 1.11
0429-30 | 1697 | 3.00 | -.15 | 0.83
DAWN- dropsonde comparisons during 2017 CPEX
Date | # of U Samples | Mean ∆z (m) | Bias (m/s) | RMSD (m/s)
ALL | 16207 | 3.11 | .08 | 1.59
Date | # of V Samples | Mean ∆z (m) | Bias (m/s) | RMSD (m/s)
All | 16207 | 3.11 | .19 | 1.61

## Slide 24
30 April 2019 Aeolus underflight
DAWN vs. Dropsondes
DAWN vs. Aeolus
10 km

## Slide 25: Conclusion
Airborne Doppler Wind Lidars, especially currently available
coherent detection systems, are meeting the challenge of
providing higher precision, higher vertical resolution and
higher horizontal resolution for space-based instrument and
mission design, data product algorithm development or
cal/val of space-based wind observing systems that
traditionally have lower precision or sample densities,
regardless of the orbiting technology. This is especially true
for cal/val over the oceans.

## Slide 26: Example of DAWN’s mapping the ABL from 10km FL
Height (km)
0 1 2 3 4 5 6 7 8 9 10
Signal Strength (dB)
12 second (~84 km) WIND-SP orbit segment

## Slide 27: Example of Single Shot Returns from DAWN during CPEX (~22m between shots; ~60m vertical resolution)
Height (km)
0 1 2 3 4 5
Signal Strength (dB)
Cloud
Small A/C roll
10 km
~85 km