## Slide 1
Chris Barnet
Science and Technology Corporation, STC
STAR Seminar: Wednesday March 6, 2019
Co-Authors: Thomas S. Pagano, NASA/JPL, Sid Boukabara (STAR),
Kevin Garrett (STAR), Kayo Ide (UMD),
Erin Jones (UMD-CICS), Yingtao Ma (UMD-CICS)
Help from: Colby Francoeur, Nadia Smith, Rebekah Esmaili (all STC)
Motivation for an experiment: can we utilize the CrIS short-wave infrared channels in data assimilation?
Notes: https://www.star.nesdis.noaa.gov/star/seminars.php
Wednesday March 6, 2019, Room 2554-2555 12:00-1:00 EST
USA participants: 866-832-9297 Passcode: 6070416
Abstract:
Advanced hyperspectral sounders such as the Advanced Infrared Sounder (AIRS), Interferometric Atmospheric Infrared Sounder (IASI) and the Cross-track Infrared Sounder (CrIS) all invested heavily in providing high signal-to-noise measurements in the short-wave infrared (SWIR) spectral region (defined here as from 3.8 to 5 microns).
The use of this spectral region is complicated by the need to handle solar radiation that is both reflected from the surface and also excites molecules in the upper stratosphere and lower mesosphere into non-equilibrium emission. The AIRS Science Team demonstrated how to properly use the SWIR to derive high-quality temperature, moisture, and trace gases with the launch of Aqua/AIRS in 2002. The NOAA-Unique Combined Atmospheric Processing System (NUCAPS) operationally deployed the AIRS algorithm for the Metop-A/IASI, S-NPP/CrIS, Metop-B/IASI, and the NOAA-20/CrIS instruments since 2008, 2011, 2012, and 2018, respectively.
This presentation will focus on the lessons learned from the NUCAPS experience and discuss the advantages, and disadvantages, of using SWIR channels. The high sensitivity (at higher operating temperatures) and uniformity of detector arrays could enable lower cost and more compact concepts to be deployed in low-Earth and geostationary orbits. This has led to the following question: could the SWIR channels replace the long-wave channels currently used within numerical weather prediction? This presentation will conclude with a discussion of an experiment to help answer that question.
Biography:
Chris Barnet’s early career was a “random walk” kind of process allowed him to be involved with many interesting topics that required finding a practical solution to the problem of the day. He started as a welder at Fermilab - an accelerator for protons - and that led to working with waveguides, superconductors, holography, radio telescopes, quasi-stellar objects, array processors, observing and modeling of the outer planets, and finally Earth remote sounding. This mixture of engineering and science may be the reason why he is now interested in finding ways to transition new algorithm concepts into operational applications.

## Slide 2: Topics for today
I am discussing the motivation behind an experiment to assimilate the short-wave infrared radiances (SWIR  2000-2800 cm-1) from the Cross-Track Infrared Sounder (CrIS)
  Topic #1: History of the SWIR instruments
  Topic #2: The Pro’s and Con’s of using the SWIR
The experiment is designed to answer the following questions:
  Can the SWIR add additional information?
    Topic #3: Radiance vs. Brightness Temperature DA
    Topic #4: Spectral Purity
    Topic #5: non-LTE
  Can the SWIR replace the LWIR for the next generation of sounding instruments?
    Topic #6: What is the future for IR sounding instruments?

## Slide 3: topic #1: A Little HIStory of hyperspectral Sounding Instruments

## Slide 4: 1980’s began the launch of microwave and infrared sounders for weather forecasting
1977 Lewis Kaplan published idea that SWIR (2000-2800 cm-1) has unique sounding properties.
  See Kaplan, Chahine, Susskind Searl 1977 Applied Optics v.16 p.322-324.
1989 Dave Wark writes the NOAA specifications for a hyperspectral infrared sounder
Makes use of Kaplan’s idea of using SWIR CO2 band
Notes: Kaplan, L.D., M.T. Chahine, J. Susskind and J.E. Searl 1977. Spectral band passes for a high precision satellite sounder. Applied Optics v.16 p.322-324.

## Slide 5: 1990’s: The AIRS Science Team is formed and implements the NOAA requirements
Advanced the design of microwave + infrared advanced sounding instruments.
Developed advanced forward models for the microwave and infrared.
  Major investment in low noise, high spectral resolution SWIR
Developed an algorithm approach that merged numerous concepts, including the use of the SWIR for sounding.
Notes: Note: the AIRS algorithm incorporated the vertical resolution concepts of Backus and Gilbert as well as smoothing and concepts of Twomey, Conrath, and Rodgers. The instrument specifications were inspired by Kaplan’s

## Slide 6: The first (and only) AIRS instrument was launched on the NASA EOS Aqua Platform May 4, 2002
AIRS
HSB
AMSU-A1(3-15)
AMSU-A2(1-2)
Delta II 7920
MODIS
Aqua Acquires 325 Gb of data per day
AMSR-E
AIRS Version.5, fully exploiting the SWIR and the basis for NUCAPS, has been operational at NASA since 2007
Notes: NOTE: 1st AMSU was launched on NOAA-15 in 1998
HSB failed in Jan. 2003 but was a copy of the MHS instrument (that would later be launched on Metop) that Brazil donated to the Aqua program.

## Slide 7: Example of 15 m band radiance measurement from AIRS 1st operational day, Sep. 6, 2002

## Slide 8: The NOAA-Unique Combined Atmospheric Processing System (NUCAPS) was envisioned in late 1990’s. NUCAPS leverages the lessons learned by NASA AIRS Team
NASA/Aqua
1:30 pm orbit
(May 4, 2002)
Suomi-NPP & JPSS
1:30 pm orbit
(Oct. 28, 2011, Nov. 18, 2017, 2021)
EUMETSAT/METOP-A,B, C
9:30 am orbit
(Oct. 19, 2006, Sep. 17, 2012, Nov. 7, 2018)
9:30 and 1:30 orbits provide information at critical times in the diurnal cycle
Discussions at 1999 ITOVS and OSA meetings led to the 2004 NOAA Research Plan to implement NUCAPS
Notes: NUCAPS concept first described in Barnet and Susskind 1999 Tech. Proc. Int'l TOVS Study Conf. v.10 p.22-33.
Full outline of the NUCAPS plan for Aqua, Metop, and NPOESS (later to be Suomi-NPP and JPSS program) was described in the NOAA STAR Research Project Plan (May 19, 2004)
The NUCAPS science code was operational at 1st light of AIRS (June 13, 2002), IASI (early 2007) and CrIS (early 2012) demonstrating the robustness of the AIRS methodology.

## Slide 9: First IASI instrument was launched on the EUMETSAT MetOp-A Satellite on Oct. 19, 2006
Soyuz 2/Fregat launcher,
Baikonur, Kazakhstan
IASI
MHS
AMSU-A1
AMSU-A2
ASCAT
HIRS
AVHRR
NUCAPS, using IASI SWIR, has been operational since Dec. 2008

## Slide 10: First CrIS/ATMS was launched on the NPP Satellite on Oct. 28, 2011
Delta-II-7920
Vandenburg AFB
VIIRS
ATMS
CERES
OMPS (electronics)
OMPS Nadir, limb
CrIS
X-band DB Antenna
X-band 300 Mb/s Antenna
S-band C+T Antenna

## Slide 11: Spectral Coverage of Thermal Sounders & Imagers (Aqua, Metop-A,B,C, Suomi-NPP, NOAA-20+)
AIRS, 2378
Channels
CrIS 2211
IASI, 8461
Channels
CO2
CO2
O3
CO
CH4
H2O

## Slide 12: What is important for sounding is signal to noise
Per channel noise is shown as noise equivalent delta temperature (NET) at a cold scene temperature (T=250 K)
NOTE: CrIS-FSR (and IASI) has higher noise in the SWIR than the LWIR
Notes: Used Dave Tobin’s Dec. 11, 2019 NEDN(FOV)
Averaged the 9 FOV’s and divided by Hamming NRF of 1.58
AIRS is CRF v.6 and IASI is the noise used in NUCAPS operations

## Slide 13: So where are we today?
It has been 42 years since Kaplan, Chahine and Susskind noted the advantage of the SWIR in sounding.
It has been 30 years since Dave Wark wrote the hyperspectral sounding requirements.
It has been 16 years since the AIRS ST demonstrated the benefits of the SWIR.
It has been 14 years NOAA laid out a plan to exploit 30+ years of hyper-spectral assets with the lessons learned from the AIRS ST.

## Slide 14: TOPIC #2: So let’s talk about the Pro’s and Con’s of using the SWIR

## Slide 15: The Advantage of High Spectral Resolution is improved Vertical Resolution (selectivity)
Sampling over rotational bands
Sounding accuracy depends on sensitivity to the vertical
temperature
gradient

## Slide 16: These instruments really measure radiance that is, energy/time/area/steradian/frequency-interval
To Convert to Brightness Temperature  Find Temperature where the Planck Function is equal to measured radiance at a given frequency.
This is what we really measure.
This is how we usually show it.
Microwave
LWIR
MWIR
SWIR

## Slide 17: The SWIR is ~3x more sensitive due to the non-linearity of Planck function
Example Brightness Temperature for Polar, Mid-Lat, and Tropical cases
% change in radiance for a 1 K change in T
SWIR changes 4-6%/K
LWIR changes 1-2 %/K
This is due to the derivative of the Planck function
Cold scenes are significantly more sensitive.

## Slide 18: The CrIS FSR LWIR & SWIR Temperature (top) and Moisture Channel Kernel Functions
Sensitivity to Temperature
Sensitivity to Water
LWIR (15 m, 650-800 cm-1)
SWIR (4 m, 2200-2700 cm-1)
CO2
N2O
CO
Water affects lower sounding channels
Negligible water sensitivity

## Slide 19: Pro’s and con’s of SWIR vs. LWIR
 | LWIR | SWIR
Interfering gases in CO2 bands | H2O, O3, HNO3 | None
Exploit the use of N2O sounding | No | YES
Vertical sounding range | 1 hPa to surface | 20 hPa to surface
Influence of solar radiation | negligible | Must handle non-LTE and surface reflection
Planck function linearity | 1st order linearity | Highly nonlinear
Instrument Noise sensitivity to scene temperature | Can Assimilate BT’s (not really true!!) | Noise is stronger function of scene T
FWHM of T(p) Kernel Fnct’s | 4 km | 2 km
Future instruments: Detector technology and optics. | Higher Power Requires Cold T’s | More COTS options
NOTE: All of the items in SWIR column been resolved by the AIRS science team & implemented in NUCAPS-IASI and NUCAPS-CrIS systems.

## Slide 20: TOPIC #3: Radiance versus brightness temperature data assimilation

## Slide 21: One of the biggest outcomes of this experiment might be communication
Data assimilation and retrievals are the same math, but there are many differences, for example:
    Retrievals do not “inflate” the observation error.
    Retrievals can explicitly add “geophysical errors.”
    Retrievals never convert observations to brightness temperature because observed radiances can go negative!
Instrument noise can be difficult to characterize exactly, but it is usually more linear in radiance space.
  Retrievals handle spectral correlations, noise as a function of scene temperature, and other effects.
Having retrieval, instrument, and DA folks in the same room, looking at details of how things are done, matters!

## Slide 22: Simplified view of how things are done
Variable | Retrievals | Data Assimilation
Observations | Radiance, Robs(n) | Brightness Temp., obs(n)
Forward Model | SARTA Rcalc(n,X) X=state | CRTM Rcalc(n,X) X=state
Conversion | G(n,X)  B/T(n, calc(n)) | x  B-1(n, Rx)
Signal, S | [ Robs(n) - Rcalc(n,X) ] / G(n,X)  obs(n) - calc(n) | obs(n) - calc(n)
Noise, N | NEN(n) / G(n,X)  NET(n, X) | NET(n)
S/N | [ obs(n) - calc(n) ] / NET(n, X) | [ obs(n) - calc(n) ] / NET(n)
When minimizing the cost function, we are effectively minimizing the square of S/N
Saying it is radiance assimilation is misleading, it really is brightness temperature assimilation.

## Slide 23: But nothing in life is free.
The instrument NET increases non-linearly for cold scene temperatures
Note that for a constant NEN
  LWIR NET varies by 3x
  MWIR NET varies by 16x
  SWIR NET varies by 100x
In the SWIR it is critical to use radiance, not brightness temperature, as the operator
Scene BT | LW NEN | LW NET | MW NEN | MW NET | SW NEN | SW NET
200 K | 0.05 | 0.09 | 0.03 | 0.65 | 0.0046 | 9.7
250 K | 0.05 | 0.04 | 0.03 | 0.12 | 0.0046 | 0.5
300 K | 0.05 | 0.03 | 0.03 | 0.04 | 0.0046 | 0.07
Note: This issue has recently been raised by Larrabee Strow & CrIS SDR Team
Notes: LWIR is using 181211tobin_nedn_snpp.dat and Hamming Apodization at 800 cm-1
SWIR is using 181211tobin_nedn_snpp.dat and Hamming Apodization at 2390 cm-1

## Slide 24: TOPIC #4: Spectral PuritY

## Slide 25: Molecular Vibrational Modes (Example: CO2)
CO2 has 4 modes of vibration. Each is quantized.
  1 is symmetric stretch (not active in infrared due to lack of dipole moment) but does interact via Fermi resonance with 2
  2 is a bending that is doubly degenerate
  3 is an asymmetric stretch
Energy of vibrational mode is given by
  Evib =  hc·k·(ik+ ½) for ik = 0, 1, 2, 
Isotope | transition | band | S | d
12C16O16O | 0000  0110 | 667.38 | 194 | 1.56
 | 0110  0220 | 667.75 | 15 | 0.78
 | 0110  1000 | 720.81 | 5 | 1.56
 | 0110  0000 | 618.03 | 4 | 1.56
 | 0220  0330 | 688.11 | 0.85 | 0.78
 | 1000  1110 | 647.06 | 0.7 | 1.56
13C16O16O | 0000  0110 | 648.48 | 2.01 | 1.56
12C18O16O | 0000  0110 | 662.37 | 0.77 | 1.56
Notes: CO2 energy levels from Middle Atmosphere Dynamics, D.G. Andrews, J.R. Holton, C.B. Leovy 1987 p.43
Table is from CO2 15μm band parameters, (Kiehl+Ramanathan, 1983

## Slide 26: Rotational Modes
The energy of rotation is quantized and given by
  Erot = hc·B·j·(j+1), j = 0, 1, 2, 3, 
But as the molecule rotates it also has centrifugal forces
  Erot = hc·(B·j·(j+1) - D·j2·(j+1)2
P-branch lines form when j = +1
Q-branch lines form when j = 0
R-branch lines form when j = -1

## Slide 27: All the Physics is Contained in a quantity called the Absorption Coefficient
The absorption coefficient is a complicated and highly non-linear function of molecule i and line j
Line Strengths, Sij, result from many molecular vibrational-rotational transitions of different molecular species and isotopes of those species(blue).
Line strength (at T=300K) of CO2, H2O, and O3 in the 15 m band.
Line strength, S, is also a function of temperature
(1-EXP(1-1.439/T))3
S(T) = S(T0)·(T/T0)·------------------------------
(1-EXP(1-1.439/T0))3
Where width of line, ij, is a function of the molecule structure (natural broadening), temperature (doppler broadening) and pressure (collisional broadening)

## Slide 28: Example of vibration rotational line strengths in 15 m band region
600 to 700 cm-1
700 to 800 cm-1
H2O
CO2
O3
N2O
HNO3
SO2
NH3
CH4
CO

## Slide 29: Example of vibration rotational line strengths in 4 m band region
2100 to 2200 cm-1
2300 to 2400 cm-1
H2O
CO2
O3
N2O
HNO3
SO2
NH3
CH4
CO
2200 to 2300 cm-1

## Slide 30: topic #5: non-LTE

## Slide 31: How big is the non-LTE effect?
This figure stolen from Zhenglong Li (CIMSS)
CRTM simulation of a channel pair difference
SWIR 2336.25 cm-1 minus LWIR 667.50
Non-LTE effect is ~5 to ~10 K in daytime
Bias in AIRS SWIR region for daytime radiances versus solar zenith angle
Need to correct for non-LTE from 2255 to 2383 cm-1
From DeSouza-Machado 2007 GRL, Fig. 3
Notes: Zhenglong’s Oct. 31, 2018 discussion page 12
CRTM Simulated Non-LTE for 2336.25 cm-1
On 7/17/2017 0000-1200 UTC

## Slide 32: We know how to correct for non-LTE.
The use of the Planck function assumes a Boltzmann distribution in the population of energy states – called thermodynamic equilibrium or LTE
Channels sensitive to high altitudes do not have enough molecular collisions to achieve equilibrium – called non-LTE
AIRS Science Team dealt with this issue and employed an algorithm to correct for non-LTE effects (DeSouza-Machado 2007 GRL)
NASA/AIRS ST and NOAA NUCAPS Teams have demonstrated that the SWIR + LWIR can be used for both day and night without introducing day-night artifacts.
Non-LTE correction is in the CRTM (Chen 2013 JAOT)
Notes: Chen, Y., Y. Han, P. Van Delst and F. Weng 2013. Assessment of shortwave infrared sea surface reflection and nonlocal thermodynamic
equilibrium effects in the Community Radiative Transfer Model using IASI data. J. Atmos. Oceanic Tech. v.30 p.2152-2160.
DeSouza-Machado, S.G., L.L. Strow, S.E. Hannon, H.E. Motteler, M. Lopez-Puertas, B. Funke and D.P. Edwards 2007. Fast forward radiative transfer modeling of 4.3 um nonlocal thermodynamic equilibrium effects for infrared temperature sounders. Geophys. Res. Lett. v.34 L01802 doi:10.1029/2006GL026684, 5 pgs.

## Slide 33: topic #6: What is The future of Infrared hyperspectral

## Slide 34: Example of technologies enabled by using SWIR: A NASA/JPL CubeSat Instrument called CIRAS
Spacecraft
(BCT)
Blackbody Assembly
Black Silicon
Immersion Grating (JPL)
Optics Assembly
(Ball)
Dewar (IDCA)
(IR Cameras)
Camera Electronics (IR Cameras)
Stepper Motor + Mirror
(Lin Eng )
Cryocoolers + Electronics (Ricor K508N )
Payload Electronics
FPA
HOTBIRD
(JPL)
Slit (JPL)
Entire satellite can fit in 6U (60x10x10 cm) enclosure!

## Slide 35: Advantage of the SWIR might be most important for future instruments
Low power {and lower noise} detectors can drive the entire design of instruments and satellites.
Low mass, power, and size will have significant implications for schedule and launch of these instruments.
 | Size (cm) | Mass (kg) | Power (W)
AIRS | 116 x 159 x 95 | 177 | 200
IASI | 120 x 110 x 130 | 236 | 210
CrIS | 80 x 47 x 66 | 147 | 106
CIRAS | 10 x 20 x 30 | 4 | 29
Notes: CIRS was a NASA/INVEST proposal in 2015

## Slide 36: Summary of the experiment
NOAA/OPPA has funded a study to study the impact of the CrIS SWIR in DA
  We will account for non-LTE, solar surface reflection, scene dependent noise, etc.
My NOAA co-authors will perform an OSSE.
  The CrIS instrument is being used as a proxy for future instrument concepts, such as CIRAS.
  CrIS-FSR is also operationally relevant to NCEP.
  We will develop QC, thinning, and bias correction schemes suitable for SWIR.
  We will also evaluate radiance data assimilation versus brightness temperature data assimilation.

## Slide 37: Questions?

## Slide 38: Documents available
cell: (301)-789-6934 email: chrisdbarnet@gmail.com
Google drive short link: http://goo.gl/twuRtW
NOTES from UMBC classes, theory of remote sounding (PHYS741) and numerical methods documentation (PHYS 640)
rs_notes.pdf (~17.5 MB, ~650 pages)
180702_cuny_barnet.pdf (10 MB, 140 slides)
phys640_s04.pdf (~8.8 MB, 370 pages)
These are living notes, or maybe a scrapbook – they are not textbooks.
Those documents refer to other documents that are also on the google drive.

## Slide 39: Apodization Alters the ILS and Spectally Correlates the Noise.
Interferometers measure interferograms (green curve) signal as a function of optical delay, 
Performing a inverse cosine transform will yield the spectrum.
Un-apodized transforms (red) have a SINC(x)=SIN(x)/x instrument line shape (ILS).
AIRS has a Gaussian ILS (black)
Apodization can produce a ILS that is localized and has small (< 1%) side lobes. But the tradeoff is that the central lobe is wider and the signal is spectrally correlated between neighboring channels
Channel Spacing | Gaussian | Hamming | Blackman
±1 | 70.74% | 62.5% | 75.5%
±3 | 25.0% | 13.3% | 31.6%
±4 | 4.43% | - | 6.57%
±5 | 0.38% | - | 0.53%
±6 | 0.025% | - | -
 | Gaussian | Hamming | Blackman
FWHM / FWHM(SINC) | 1.682 | 1.5043 | 1.905
Random Noise reduction | 1.735 | 1.586 | 1.812
Maximum Side-Lobe | 0.45% | 0.73% | 0.12%
% of signal in central Lobe | 95.1% | 87.5% | 99.8%