## Slide 1: Fellowship of the Rain (Gauge Network)
Douglas Miller
Atmospheric Sciences Department
UNC Asheville
Ana Barros
Civil Engineering Department
Duke University
In collaboration with…

## Slide 2: Outline
High elevation rain gauge network in the Pigeon River Basin and Great Smoky Mountains National Park (Duke GSMRGN)
  Founding
    Why the Pigeon River Basin?
    Purpose
    Installation and maintenance and challenges
  Findings
    Pigeon River Basin
    Pigeon v. Coweeta River Basin
  Future
    Climate-related questions

## Slide 3
Hurricane Ivan
Hurricane Frances
Flood Data
Courtesy: John Fargher, P.E.

## Slide 4
September 18, 2004
The Pigeon River
Courtesy: John Fargher, P.E.

## Slide 5
Aerial Photographs
1992
2004
Courtesy: John Fargher, P.E.

## Slide 6
Courtesy: John Fargher, P.E.

## Slide 7: Original purpose - funding
NASA
  Provide ground validation (GV) at high elevation locations in the mid-latitudes for NASA’s Global Precipitation Mission (GPM)

## Slide 8
GPM LAUNCH: 27 FEBRUARY 2014, 1:37 PM EST, TANEGASHIMA SPACE CENTER, JAPAN
Improves upon the capabilities of the Tropical Rainfall Measurement Mission (TRMM), a joint NASA-JAXA mission launched in 1997 and still in operation.
Expands coverage area from 40°N to 40°S (TRMM) to from the Arctic Circle to the Antarctic Circle.
Detect light rain and snowfall, a major source of available fresh water in some regions.
Collect information that unifies and improves data from an international constellation of existing and future satellites by mapping global precipitation every three hours.
http://www.nasa.gov/mission_pages/GPM/main/#.Ux9ynM65Hws
Wilson et al. (2014)
Notes: TRMM stands for Tropical Rainfall Measurement Mission
TRMM revisits area on average once a day
8

## Slide 9
GPM Ground Validation Program
Provide ground and airborne precipitation datasets supporting physical validation of satellite-based precipitation retrieval algorithms
Determine the measurement uncertainty for GPM measurements to allow users of GPM data to interpret observations
Improve the retrieval algorithms used by GPM and future space-based precipitation measurement missions
Improve understanding of precipitation processes and the ground-based GV measurements themselves, which have historically been beset with difficulties
Purpose
seek to advance our physical understanding of precipitation processes and assure consistency between this understanding and the representation of those physical processes in NASA GPM retrieval algorithms
Wilson et al. (2014)

## Slide 10
Installation and Maintenance
pc: Daniel Martin

## Slide 11
Duke University Great Smoky Mountain Rain Gauge Network (Duke GSMRGN)
Miller et al. (2018)
2008
2007
2009
Notes: 11

## Slide 12
Methodology
Notes: 12

## Slide 13
32 gauges
Methodology
6570 ft
3398 ft
Notes: 13

## Slide 14
Southern Appalachians
Clingmans Dome [3]
2024 m (6643 ft)
Mt. Guyot [4]
2018 m (6621 ft)
Mt. Mitchell [1]
2037 m (6684 ft)
Pigeon River Basin (PRB)
1823 km2 (704 sq mi)
Notes: 2037 m = 79130.7 Pascals (U.S. Standard Atmosphere)
Mount Craig is 2nd highest peak east of the Mississippi River
14

## Slide 15
Backcountry Horsemen of NC
http://www.hikinginthesmokys.com/_wizardimages/at%20-%20elev%20profile.jpg
2354
4525
Installation

## Slide 16
Day One

## Slide 17
Day One
pc: Daniel Martin

## Slide 18
Day Two
pc: Daniel Martin

## Slide 19
Day Two
pc: Daniel Martin

## Slide 20
2354
http://www.hikinginthesmokys.com/_wizardimages/at%20-%20elev%20profile.jpg
4525
6621
Final Gauge
pc: Daniel Martin

## Slide 21
Finished!! 12 June 2009
pc: Daniel Martin

## Slide 22
Maintenance
pc: Daniel Martin

## Slide 23
Maintenance

## Slide 24
Maintenance

## Slide 25
Maintenance

## Slide 26
Maintenance

## Slide 27
Maintenance

## Slide 28
Challenges

## Slide 29
Challenges

## Slide 30
Challenges

## Slide 31
Challenges
pc: Daniel Martin

## Slide 32
Challenges
https://www.hgtv.com/outdoors/gardens/animals-and-wildlife/the-gray-squirrel-411

## Slide 33
Challenges
pc: Daniel Martin

## Slide 34
Challenges
pc: Daniel Martin

## Slide 35
Challenges
pc: Daniel Martin

## Slide 36
Challenges
http://blizzard.atms.unca.edu/dmiller/MFDC0135.AVI

## Slide 37
Challenges
pc: Daniel Martin

## Slide 38
Challenges

## Slide 39
Challenges

## Slide 40
Challenges

## Slide 41
Challenges

## Slide 42: Local Research
  Findings…

## Slide 43: Findings
IPHEx
Wilson et al. (2014)
1 May – 15 June 2014

## Slide 44: Findings
Barros, Ana P, Douglas Miller, Anna M Wilson, Gregory Cutrell, Malarvizhi Arulraj, Paul E. Super and Walter A Petersen. 2017. GPM Ground Validation Southern Appalachian Rain Gauge IPHEx [indicate subset used]. Dataset available online from the NASA Global Hydrology Resource Center DAAC, Huntsville, Alabama, U.S.A. DOI: http://dx.doi.org/10.5067/GPMGV/IPHEX/GAUGES/DATA301

## Slide 45: Background on Atmospheric Rivers
  In the western United States…

## Slide 46: Atmospheric River
http://glossary.ametsoc.org/wiki/Atmospheric_river
A long, narrow, and transient corridor of strong horizontal water vapor transport that is typically associated with a low-level jet stream ahead of the cold frontof an extratropical cyclone. The water vapor in atmospheric rivers is supplied by tropical and/or extratropical moisture sources…Horizontal water vapor transport in the midlatitudes occurs primarily in atmospheric rivers and is focused in the lower troposphere.
IVT = Integrated Vapor Transport

## Slide 47: Background on Atmospheric Rivers
  In the southeastern United States…

## Slide 48
Moore et al. (2012)
1 – 2 May 2010
slow-moving or static supply of moisture from the tropics

## Slide 49: Climatology in SE U.S.
Lavers and Villarini (2015)
“The Appalachian Mountains are clearly visible as a low AR fraction region dividing relatively high percentages along the U.S. East Coast and the central United States.”

## Slide 50: Background
S.E. U.S. (SEUS) findings…
IVT ~500 kg m-1 s-1 reasonable threshold for defining ARs
clear connection between ARs and heavy precipitation events in non-summer months
AR conditions in SEUS have a less direct influence on heavy precipitation relative to the U.S. west coast
Mahoney et al. (2016)
Jan. 2002 – Dec. 2011

## Slide 51: Findings…
  Pigeon River Basin

## Slide 52: Methodology
Rainfall accumulation binned in 6-h periods
0000 UTC
0600 UTC
1200 UTC
1800 UTC
0000 UTC
g #1
g #32
.
.
.

## Slide 53: Methodology
Rainfall events (observed by the Duke GSMRGN)
  Rank events by event total per gauge accumulation
  Extreme (top 2.5%) rainfall events
  Normal (middle 33%) rainfall events

## Slide 54: Methodology
Investigate systematic differences between Extreme and Normal rainfall events (“Connections”)
  Atmospheric Rivers (ARs)
  Observed flooding at Newport, TN river gauge
  Storm event reports in TN, NC along common state border

## Slide 55
Methodology
Using 6-h GFS analysis (0.5o x 0.5o) grids and IVT study domain…
highest IVT contour meeting Mahoney et al. (2016) shape criteria (at least 1500 km long, no wider than 1500 km)
average maximum IVT value for three consecutive GFS analyses (12+ h) at least 500 kg m-1 s-1
IVT** study domain
Methodology
IVT** = Integrated Vapor Transport (vapor movement in lowest layer)

## Slide 56: Results

## Slide 57
Integrated Vapor Transport
GFS gridded analyses
NOAA - NOMADS
(moderate flooding)
0000 UTC 21- 0600 UTC 24 December 2013
[kg m-1 s-1]

## Slide 58
(moderate flooding)
500 hPa level Geo Ht / Temp / WS
NOAA - SPC
21- 24 December 2013

## Slide 60: Findings
Do Atmospheric Rivers impact the southern Appalachians?
  Half of Extreme events are AR-influenced
    Most likely in cool season environments
      Slow-moving high amplitude atmospheric wave
        Rapidly moving humid air at low-levels (from the Gulf of Mexico)
  Extreme events having no AR-influence
    Most likely in warm season environments
      Cut-off low level cyclone southwest of southern Appalachians
        Low-level winds blow normal to mountains – orographically-enhanced precipitation

## Slide 61: Findings
Do Atmospheric Rivers impact the southern Appalachians?
  12-25% ARs are associated with a societal hazard (flooding, flash flooding, heavy rainfall reports)
  Normal rainfall events with an AR, not associated with a societal hazard? [“non-threatening” ARs]

## Slide 62: Climatology [8-yr]
Seasonal count of number of ARs impacting the IVT study domain using available 11463 GFS 6-h analysis periods of the 8-yr study (of 11688 maximum 6-h periods; 98.1% of a complete archive) [1 July 2009 – 30 June 2017].
Meteorological Season | AR Events | 6-h Periods | Avg Duration (h)
Winter (DJF) | 79 | 451 | 34.25
Spring (MAM) | 49 | 258 | 31.59
Summer (JJA) | 24 | 175 | 43.75
Autumn (SON) | 40 | 247 | 37.05
Total/avg | 192 | 1294 | 35.34
Notes: snd_diag_look
/usr/local/www/html/arisa/data/soundings/analysis

## Slide 63: Findings…
  Comparison between the Pigeon River Basin (PRB) and the Coweeta River Basin (CRB)…

## Slide 64: Expanded view – two river basins
Methodology
  Map of pigeon and coweeta river basin boundaries embedded in elevation map of western NC
Pigeon River Basin
Upper Little Tennessee Basin
Coweeta River Basin

## Slide 65
Methodology
  Pigeon River Basin – displaced north and west of the Blue Ridge escarpment
  Coweeta River Basin – adjacent to the Blue Ridge escarpment
Methodology

## Slide 66: 8-yr comparison; PRB v. CRB
Results
  Number of extreme (top 2.5%) rain events of the 8-yr study [1 July 2009 – 30 June 2017].
River Basin | AR-influenced | TC-influenced | NOT AR- or TC-influenced | Total
Pigeon | 23 (53.5%) | 3 (7.0%) {Ida, Lee, Andrea} | 17 (39.5%) | 43
Coweeta | 20 (83.3%) | 2 (8.3%) {Ida, Lee} | 2 (8.3%) | 24
TC = tropical cyclone
Notes: 1464/19 = tave (PRB) = 77.05 h,
1260/18 = tave (CRB) = 70.00 h

## Slide 67: 8-yr comparison; PRB v. CRB
Results
  Seven rainfall events qualify as extreme in the Coweeta River Basin and less-than-extreme in the Pigeon R.B.
    Six events = AR influenced (5 Feb 2012, 16 Apr 2011, 28 Nov 2011, 14 Oct 2014, 18 Nov 2015, and 3 Feb 2016)
    One event = squall line and severe weather (26 Oct 2010)
  Examination of geopotential height and precipitable water composite means and anomalies of
    six AR-influenced extreme rainfall events (CRB)
    16 AR-influenced extreme rainfall events (PRB, Miller et al. 2018)

## Slide 68: Expanded view – two river basins
Results
  Four panel 850 (a) cow AR, (c) duke AR and PW (b) cow AR, (d) duke AR geopotential composite mean
  Four panel 850 (a) cow AR, (c) duke AR and PW (b) cow AR, (d) duke AR geopotential composite anom
850 hPa
P Wat
Composite means
P Wat
850 hPa
PRB, N=16
PRB
CRB, N=6
CRB

## Slide 69: Expanded view – two river basins
Results
  Four panel 850 (a) cow AR, (c) duke AR and PW (b) cow AR, (d) duke AR geopotential composite mean
  Four panel 850 (a) cow AR, (c) duke AR and PW (b) cow AR, (d) duke AR geopotential composite anom
850 hPa
P Wat
Composite anomalies
850 hPa
P Wat
PRB
PRB, N=16
CRB, N=6
CRB

## Slide 70: 8-yr comparison; PRB v. CRB
Results
  Disagreement between two river basins on ‘extreme’ events
    Much smaller record (8-yr [v. 82-yr]) in the Pigeon River Basin
    Difference in position relative to the Blue Ridge escarpment
    Relative landform homogeneity of the Coweeta River Basin; 8-9 [32] gauges spread over 16.26 km2 [1823 km2, PRB]
  Composite weather AR pattern differences
    Southwesterly flow favors extreme events in the PRB
    Southerly flow inhibits extreme events in the PRB

## Slide 71: Expanded view – two river basins
Methodology
  Map of pigeon and coweeta river basin boundaries embedded in elevation map of western NC
http://www.wncvitalityindex.org/topography/mountain-topography-and-geomorphology
Richland Balsam, 1845 m (6053 ft)

## Slide 72: Future…
  Hypothesis; another way Atmospheric Rivers can cause a disruption in the southern Appalachian Mountains…

## Slide 73: Future
Methodology
  Longer time-scale precipitation events; Elevated Rain Time Clusters [ERTCs]
Δt = 30-h
Notes: N = 4733 SRTC events since 4 June 1936

## Slide 74: Expanded view – mud slides, debris flows
Results
  NCEP/NCAR reanalysis composite means and anomalies of july 2013…
300 hPa
500 hPa
Composite means – July 2013
850 hPa
P Wat

## Slide 75: Expanded view – mud slides, debris flows
Results
  NCEP/NCAR reanalysis composite means and anomalies of july 2013…
300 hPa
500 hPa
850 hPa
P Wat
Composite anomalies – July 2013

## Slide 76: Future – mud slides, debris flows
Results
  Animation of July 2013 AR
IVT – GFS 6-h analyses

## Slide 77: Future…
‘Maya Corridor’ hypothesis
  ridge-building provided via the diabatic process of latent heat release as the sub-tropical moisture of the ARs was converted to cloud water and precipitation
  as the ridge continued to build, the large-scale weather pattern became increasingly stagnant
  repeated propagation of successive ARs over the same pathway and increased ridge-building through continued latent heating
  provided a mechanism for ‘training’ rainfall events over the southern Appalachian Mountains that pre-conditioned the soil and/or triggered landslides

## Slide 78: Future…
Warm season studies (Duke GSMRGN is now past 10 year mark)
  Regional WRF simulation of July 2013 – impact of diabatic heating – confirm/refute Maya Corridor hypothesis
  Identify convection “hot spots” in the PRB with events stratified by the 850 – 700 hPa layer winds
  Systematic change of the initiation time of convection in the PRB?

## Slide 79
Near Purchase Knob, credit: Michael Goldsbury
Acknowledgements
Special thanks to Paul Super, Jim Renfo, and everyone in the Great Smoky Mountains NP for your invaluable help and cooperation!

## Slide 80: References
Lavers, D. A., and G. Villarini, 2015: The contribution of atmospheric rivers to precipitation in Europe and the United States. J. Hydrology, 522, 382-390.
Miller, D.K., C.F. Miniat, R.M. Wooten, and A.P. Barros, 2019: An expanded investigation of atmospheric rivers in the southern Appalachian Mountains and their connection to landslides. Atmosphere, 10, 71 (DOI:10.3390/atmos10020071).
Miller, D.K., D. Hotz, J. Winton, and L. Stewart, 2018: Investigation of atmospheric rivers impacting the Pigeon River Basin of the southern Appalachian Mountains. Wea. Forecasting, 33, 283-299 (DOI:10.1175/WAF-D-17-0060.1).
Moore, B. J., P. J. Neiman, F. M. Ralph, and F. E. Barthold, 2012: Physical processes associated with heavy flooding rainfall in Nashville, Tennessee, and vicinity during 1–2 May 2010: The role of an atmospheric river and mesoscale convective systems. Mon. Wea. Rev., 140, 358-378.
Neiman, P. J., F. M. Ralph, G. A. Wick, J. D. Lundquist, and M. D. Dettinger, 2008: Meteorological characteristics and overland precipitation impacts of atmospheric rivers affecting the west coast of North America based on eight years of SSM/I satellite observations. J. of Hydrometeorology, 9, 22-47.
Mahoney, K.M., D. L. Jackson, P. Neiman, M. Hughes, L. Darby, G. Wick, A. White, E. Sukovich, R. Cifelli, 2016: Understanding the role of atmospheric rivers in heavy precipitation in the southeast United States. Mon. Wea. Rev., 144, 1617-1632.
Wilson, A. M., and A. P. Barros, 2014: An investigation of warm rainfall microphysics in the southern Appalachians: Orographic enhancement via low-level seeder–feeder interactions. J. Atmos. Sci., 71, 1783–1805, https://doi.org/10.1175/JAS-D-13-0228.1.

## Slide 81: extra References
Cordeira, J. M., F. M. Ralph, and B. J. Moore, 2013: The development and evolution of two atmospheric rivers in proximity to western North Pacific tropical cyclones in October 2010. Mon. Wea. Rev., 141, 4234–4255, doi:10.1175/MWR-D-13-00019.1.
Guan, B., D. E. Waliser, and F. M. Ralph, 2018: An intercomparison between renalysis and dropsonde observations of the total water vapor transport in individual atmospheric rivers. J. Hydrometeor., 19, 321–337, doi:10.1175/JHM-D-17-0114.1.
—, and —, 2015: Detection of atmospheric rivers: Evaluation and application of an algorithm for global studies. J. Geophys. Res. Atmos., 120, 12 514–12 535, doi:10.1002/2015JD024257.
Ralph, F. M., P. J. Neiman, and G. A. Wick, 2004: Satellite and CALJET aircraft observations of atmospheric rivers over the eastern North Pacific Ocean during the winter of 1997/98. Mon. Wea. Rev., 132, 1721–1745, doi:10.1175/1520-0493(2004)132<1721:SACAOO>2.0.CO;2.
—, and Coauthors, 2017: Dropsonde observations of total water vapor transport within North Pacific atmospheric rivers. J. Hydrometeor., 18, 2577–2596, doi:10.1175/JHM-D-17-0036.
Zhu, Y., and R. E. Newell, 1998: A proposed algorithm for moisture fluxes from atmospheric rivers. Mon. Wea. Rev., 126, 725–735, doi:10.1175/1520-0493(1998)126<0725:APAFMF>2.0.CO;2.

## Slide 82
Details of slides #10 – 41 are described in Chapter 11 of the book to be published in 2020…
University of California Press