## Slide 1: GLM Product Evaluation and Highlights of My Research at CICS
Ryo Yoshida
Satellite Program Division, Observation Department
Japan Meteorological Agency (JMA)
STAR Seminar, October 24, 2019

## Slide 2: Overview of my research visit
“Japanese Government Short-Term Overseas Fellowship Program” sponsored by the National Personnel Authority of Japan
  Period: Nov. 5, 2018 - Nov. 3, 2019
NESDIS accepted me at CICS, based on the framework of the NESDIS-JMA high-level letter exchange on information exchange regarding GOES-R Series & Himawari-8/9
Research topics: GLM & NOAA’s advanced efforts on satellites
I deeply appreciate NESDIS’s giving me this great opportunity

## Slide 3: Contents
Overview of JMA and Himawari satellites
Highlights of my research at CICS
GLM product evaluation

## Slide 4: 1. Overview of JMA and Himawari satellites

## Slide 5: What JMA is
Safety of transportation
Development and prosperity of industry
Prevention and mitigation of natural disasters
International cooperation
Japan’s national meteorological service, whose ultimate goals are
prescribed by the Meteorological Service Act.

## Slide 6: What JMA does
Weather observations
Weather forecasts and warnings
Aviation & marine weather services
Climate & global environment services
Monitoring seismic & volcanic activity & tsunamis

## Slide 7: JMA’s weather observation systems
Surface Observations
Surface observations
Doppler radars
Geostationary satellites
Upper air observations
Observations for Aviation
20 doppler radars
>1300 stations
16 radiosonde stations
33 wind profilers

## Slide 8: JMA’s weather prediction system
JMA’s world-class operational supercomputer system runs global & regional models.
 | Global Spectral Model (GSM) | Meso-Scale Model (MSM) | Local Forecast Model (LFM) | Global Ensemble (GEPS) | Meso-scale Ensemble (MEPS) | Seasonal Ensemble (CPS2)
Forecast domain | Global | Regional | Regional | Global | Regional | Global (Coupled)
Horizontal resolution | TL959 (0.1875 deg) | 5km | 2km | TL479 / TL319 (0.375 / 0.5625 deg) | 5km | Atmos: 1.125 deg Ocean: 0.3-0.5x1 deg
https://www.top500.org/lists/2019/06/

## Slide 9: Himawari series satellites
April 6, 1978
July 14, 1977
Satellite | Obs period
GMS (Himawari) | 1978 – 1981
GMS-2 (Himawari-2) | 1981 – 1984
GMS-3 (Himawari-3) | 1984 – 1989
GMS-4 (Himawari-4) | 1989 – 1995
GMS-5 (Himawari-5) | 1995 – 2003
GOES-9 | 2003 – 2005
MTSAT-1R (Himawari-6) | 2005 – 2010
MTSAT-2 (Himawari-7) | 2010 – 2015
Himawari-8 | 2015 – (2022)
Himawari-9 | (2022) – (2029)
Covering the Asia-Pacific region for over 40 years

## Slide 10: Himawari-8 and -9
The latest generation of Himawari series satellites.
  Himawari-8 in operation since 2015.
  Himawari-9 on standby in orbit, and scheduled to be operational in 2022.
  Compose a twin satellite system until 2029.

## Slide 11: AHI aboard Himawari-8/9
Himawari-8/9 each carry the Advanced Himawari Imager (AHI), an ABI-class 16-spectral-band imaging instrument.

## Slide 12: AHI frequent observations
AHI generates a full disk image every 10 minutes, while providing regional observations with 2.5 min and 30 sec intervals.
1000 km x 1000 km
500 km x 1000 km
1000 km x 2000 km

## Slide 13: National weather services using Himawari-8
Observation Area of Himawari-8/9
HimawariCast
32 users
Russia
Mongolia
Korea
China
Hong Kong, China
Macau
Nepal
Bhutan
Bangladesh
Myanmar
Laos
Sri Lanka
Thailand
Vietnam
Cambodia
Malaysia
Singapore
Indonesia
Philippines
Brunei
Palau
Timor-Leste
Micronesia
Papua New Guinea
Hawaii (USA)
Solomon Islands
Kiribati
Tuvalu
Fiji
Samoa
Cook Islands
Tonga
Vanuatu
New Caledonia (Fr.)
Australia
New Zealand
(As of May 2018)
Web service
42 areas including
Timor-Leste & Cook Islands
HimawariCloud
21 users and
NESDIS & EUMETSAT
13

## Slide 14: Himawari-8 products for NWP centers
The Himawari-8 AMV & CSR products are provided to NWP centers via the WMO Global Telecommunication System (GTS).
ECMWF Website: https://www.ecmwf.int/en/forecasts/quality-our-forecasts/monitoring-observing-system#Satellite
AMV and CSR data used in ECMWF’s assimilation system

## Slide 15: Next Himawari planning
Himawari-8/9 will complete the observation operation in 2029.
JMA has undertaken feasibility studies of their follow-on satellites.
 | USA | Europe | China | Korea
Multi-spectral VIS/IR imagery with rapid repeat cycles | GOES-R series/ ABI | MTG I series [20212]/ FCI | FY-4 series/ AGRI | GK-2A/AMI
IR hyperspectral sounders |  | MTG S series [20232]/ IRS | FY-4 series/ GIIRS | 
Lightning mappers | GOES-R series/ GLM | MTG I series [20212]/ LI | FY-4 series/ LMI | 
UV/VIS/NIR sounders | TEMPO [20221] | MTG S series [20232]/ UVN (Sentinel-4) |  | GK-2B [20203]/ GEMS
[ ] indicate planned launch year based on:
Missions (to be) implemented by satellite operators
Vision for WIGOS 2040
(Geostationary core instruments)
1 NASA’s press release (July 22, 2019)
2 EUMETSAT’s website (as of July 2019)
3 CGMS-47 KMA-WP-01 (May 2019)

## Slide 16: 2. Highlights of my research at CICS

## Slide 17: Highlights of my research at CICS
Study on GLM
  Space system & data processing (with GOES-R Data Book)
  Product evaluation
  Data use in NOAA
Study on cost benefit analysis (CBA) of weather satellites
  Existing Metop-SG CBA & JPSS CBA
  Trial CBA for a hypothetical IR sounder on Himawari
Study on NOAA’s approach for commercial satellites
  Commercial Weather Data Pilot (with NOAA’s report to the Congress)
  Weather Research and Forecasting Innovation Act of 2017
Study on NOAA’s Cooperative Institutes
  General framework (with CI Handbook)
  Research activities (with CICS annual report)

## Slide 18: Metop-SG CBA
Socio-economic benefits of weather information in Europe was assessed for three benefit areas:
  Protection of Property and Infrastructure
  Added Value to the European Economy
  Private Use by European citizens
Socio-economic benefits of Metop-SG was estimated by prorating the weather information benefits based on Metop contribution to forecast skill
EUMETSAT (2014)
Value of
weather info.
Contribution to forecast
Value of
Metop-SG
X
=

## Slide 19: Metop-SG benefit assessment
Annual socio-economic benefits of weather information
mainly based on Hallegatte, S. (2012) etc
Metop contribution to forecast skill 8 %
based on ECMWF’s data denial experiments
B/C = 5 ~ 20
where C = ~€3 billion
Metop-SG benefits for 20 years

## Slide 20: JPSS benefit assessment
Benefit of weather information was assessed by top down analysis using GDP and assumed parameters
JPSS contribution to weather forecasts assessed by the WMO OSCAR database
Mehta, A., 2015 AMS Annual Meeting

## Slide 21: CBA for a “hypothetical” IR sounder on Himawari
Socio-economic benefits of weather information in Japan was estimated by scaling those of Europe:
  Protection of Property and Infrastructure -> proportional to GDP
  Added Value to the European Economy -> proportional to GDP
  Private Use by European citizens -> proportional to # of households
B/C is derived as a function of a hypothetical IR sounder contribution to forecast skill.
  Life time and life cycle cost of the hypothetical IR sounder were assumed to be the same with the Himawari-8/9 system

## Slide 22: Benefit analysis in Japan
Annual benefit of weather information
Benefit of the hypothetical sounder for a 15-year mission life cycle
Benefit area | Minimum | Likely | Derivation
Protection of Property and Infrastructure | 58.2 | 246.4 | =[Value in EU27]x[GDP ratio JP/EU27]
Added Value to the European Economy | 448.0 | 1836.7 | =[Value in EU27]x[GDP ratio JP/EU27]
Private Use by European citizens | 133.6 | 501.1 | =[Value in EU27]x[# household ratio JP/EU27]x[exchange ratio ¥/€]
Total | 639 | 2584 | 
Unit: billion JPY/Year
f: contribution to forecast skill
g: Annual GDP increase rate (1%)
r: Annual discount rate (4%)

## Slide 23: CBA result of the hypothetical IR sounder
B/C = 4.6~18.5, for a contribution of 5%
A reasonable contribution can be determined by OSSE
Contribution to forecast skill [%]
4.6
18.5
5%

## Slide 24: For refining this CBA
More realistic benefit assessment
  Benefits of weather information must be dependent on countries
  Benefits in Japan would not be derived correctly by scaling European result.
    (e.g. Typhoons need to be considered for Japan)
  Bottom-up approach is required
  Contribution to forecast skill is determined by numerical experiments
  (e.g. OSSE)
More realistic cost assessment

## Slide 25: 3. GLM product evaluation
This work was conducted in coordination with
the GLM science team at CICS led by Dr. Scott Rudlosky

## Slide 26: Geostationary Lightning Mapper (GLM)
Optical lightning sensor aboard GOES-R Serie satellites
Continuous & hemispherical coverage (up to 54 deg N/S)
Detection of both intra-cloud (IC) and cloud-to-ground (CG) lightning
  No discrimination between IC & CG
Image: GOES-R Series Data Book
GLM sensor design parameters | 
# of CCD pixels | 1372 x 1300
Frame rate | 2 ms
Ground sample distance | 8 km (Nadir) 14 km (FOV edge)
Wavelength | 777.4 nm

## Slide 27: GLM Level 2 product
Event: Pixel-level detection exceeding the threshold in one frame
Group: 1 or more events in adjacent pixels in one frame
Flash: 1 or more groups separated by less than 330 ms and 16.5 km
Image: GLM Definitions and Detection Method Quick Guide
GLM Level 2 product maturity |  | 
Status | GOES-16 | GOES-17
Launch | Nov 19, 2016 | Mar 1, 2018
Beta | June 9, 2017 | Oct 3, 2018
Provisional | Jan 19, 2018 | Dec 20, 2018
Full | Nov 1, 2018 | 

## Slide 28: GLM L2 product evaluation
A: Flash geographical distribution
B: Flash detection efficiency
  B-1: GLM vs GLD360
  B-2: GLM vs ENTLN
C: Group timing & location

## Slide 29: A: Flash geographical distribution

## Slide 30: Flash density maps (MAM 2019)
GLM16 flashes
GLM17 flashes
GLD360 strokes
Generally consistent with each other
GLM false detections (e.g. GLM16’s Bahama bars)

## Slide 31: GLM false flashes (MAM 2019)
GLM17
GLM16
Bahama bars (daytime), Solar intrusions (midnight), Solar glints (morning/evening)
Westward moving daytime artifacts (GLM17 > GLM16)
Flash density hourly variation in nadir local time

## Slide 32: Flash density maps (JJA 2019)
GLM16 flashes
GLM17 flashes
GLD360 strokes
False detections reduced by updating ground processing for G16 & G17
  Contrast Leakage Algorithm activated (Apr. 30) to reduce jitter noise
  2nd-level Threshold Algorithm updated (Apr. 30) to reduce Bahama bars
  Blooming Filter activated (Jul 25) to reduce solar glints and intrusions

## Slide 33: Before Blooming Filter activated (Jul. 2019)
GLM17
GLM16
Solar glints are apparent

## Slide 34: After Blooming Filter activated (Aug. 2019)
GLM17
GLM16
Solar glints are mitigated by Blooming Filter

## Slide 35: B: Flash detection efficiency

## Slide 36: Flash detection efficiency
Flash detection efficiency (DE) indicates the ability to detect flashes
GLM DE relative to a ground-based network (GN)
Detection criteria: flash separation less than 25 km and 0.1 s.
AND
Time
GN flash
GLM flash
GLM flash
GN flash
< 25 km
Spatial separation
Temporal separation
< 0.1 s

## Slide 37: B-1: GLM DE relative to GLD360
GLM16 & GLM17 DE for overall FOV were examined using GLD360
GLD360 is designed to globally detect >80 % CG with VLF sensors
GLD360 stroke density for May 2011 to May 2015 (Vaisala, 2015)
Acknowledgement:
GLD360 used in this study were provided by Vaisala.

## Slide 38: GLM DE relative to GLD360 (Mar-Aug, 2019)
GLM16 DE
GLM17 DE
GLM DEs are maximized over the oceans and the South America
GLM DE depression over high-boresight-angle CONUS (GLM16: NW, GLM17: NE)
GLD360 pixels with DE < ~30% generally coincide with GLM false detections
GLD360 DE

## Slide 39: DE Monthly variation
GLM16/17 DE decreases in spring & summer, when lightning activity increases over CONUS.
Note: DE is dependent on matching criteria (larger criteria, larger DE)
  Need to focus on variance/difference rather than absolute values

## Slide 40: B-2: GLM DE relative to ENTLN
GLM16 DE variance was examined using ENTLN flashes.
  IC/CG difference & diurnal variation
ENTLN is
  Earth Networks Total Lightning Network
  Designed to detect both IC & CG
  with wideband (1Hz to 12MHz) sensors
  High IC detection efficiency over CONUS.
Estimated ENTLN IC DE (Liu and Heckman, 2012)
Acknowledgement:
ENTLN data used in this study were provided by Earth Networks, Inc.

## Slide 41: GLM16 DE for ENTLN IC & CG (Dec-Aug, 2019)
GLM DE for IC (DEIC)
GLM DE for CG (DECG)
  DE depression over NW CONUS is more clear for IC
  DEIC < DECG over CONUS
DEIC - DECG

## Slide 42: Diurnal variation over CONUS
GLM and ENTLN flashes are maximized in the late afternoon (17-18 local time), associated with day-time thermal convections.
GLM DE decreases during the daytime
  Peak-to-peak diurnal variation of GLM DE is larger for IC (0.18) than CG (0.13)
0.18
0.13

## Slide 43: Cloud light blockage effect
GLM’s flash underestimation due to cloud light blockage was reported in evaluation efforts.
GLM DE dependence on cloud development was examined using the ABI cloud top temperature product (CTTABI).
Dr. Stano’s report at the 2019 AMS annual meeting:
https://ams.confex.com/ams/2019Annual/meetingapp.cgi/Person/88040

## Slide 44: Dependence on cloud top temperature
DEIC
-10 < CTTABI < -30
-30 < CTTABI < -50
-50 < CTTABI < -70
-70 < CTTABI < -90
DECG
DE decreases as CTTABI decreases

## Slide 45: Local analysis over CONUS
A
B
A
B
DEIC
b)
a)
GLM DE decreases as CTTABI decreases to ~0.2 (A) & ~0.1 (B)
DE difference between IC and CG becomes small as CTTABI decreases

## Slide 46: C: Group timing & geolocation

## Slide 47: Group timing and geolocation accuracy
Peak timing difference (-0.7 ms) is less than the GLM flame rate (2.0 ms).
Peak distance (3.25 km) is less than the GLM ground sample distance (8~14 km).
Geolocation difference [km]
ENTLN - GLM timing difference [ms]

## Slide 48: New parallax correction
Parallax in the GLM L2 product is corrected by ground processing using a static height model (lightning ellipsoid).
A new correction method using the ABI cloud top height product (CTHABI) was developed.
Observed
Earth axis
h=6km
h=14km
Lightning ellipsoid
Actual

## Slide 49: Parallax correction by ABI cloud top height
Peak error: CTHABI (2.75 km) < Lightning Ellipsoid (3.25 km)
Lightning Ellipsoid is a reasonable way for parallax correction
Geolocation error [km]

## Slide 50: Parallax correction by ABI cloud top height
(a) Lightning ellipsoid
CTHABI reduces parallax location errors near the edge of FOV
(b) ABI could top height

## Slide 51: Summary of GLM L2 product evaluation
A: Flash distribution analysis
  GLM flash distributions were consistent with GLD360
  Mitigation efforts significantly reduced GLM false detections
B: Flash detection efficiency (DE) analysis
  GLM’s high & broad detection capability
  DE depression over high-boresight-angle CONUS
  DEIC < DEGC & DEDay < DENight over CONUS
  DE decreases as CTTABI decreases
C: Group timing & location validation
  Peak errors not exceeding GLM’s sampling rate & distance
  Further improvement of parallax correction provided by CTHABI

## Slide 52
Thank you for your attention!
GOES-16
GOES-17
Himawari-8
Images created by RAMMB/CIRA SLIDER